Amateur Radio – Technician Class Subelement 6 & 7
1. Tate Belden – KA7O
2. ka7o@casperarc.net
3. Casper Amateur Radio Club – W7VNJ
4. http://casperarc.net

---
Subelement 6
- Electrical Components
- Circuit Diagrams
- Component Functions
- 4 questions
- 4 groups

---
Pretty much names and function
- A Resistor resists the flow of DC current
- A Potentiometer is a variable resistor, often used as a volume control
- Inductors store energy in a magnetic field and are often based on a coil of wire
- Capacitors store energy in an electrical field
- Capacitors are made of conductive surfaces separated by an insulator

---
More names and functions
- Switches are simply ways to connect or disconnect circuits
- Fuses protect other components from overload
- Non-rechargeable chemistry
  - Carbon-zinc
- Rechargeable battery chemistries include:
  - Nickel-Metal Hydride (NIMH)
  - Lithium Ion (Li-ion) or Lithium Polymer (LiPo)
  - Lead Acid (LA) or Sealed LA (SLA), may be Gel-cell

---
Semiconductors
- Basic principles of solid state devices
  - diodes and transistors
- Transistors act as ‘switches’ operated by an external current or voltage. Can be proportional so are useful for amplifiers
- Diodes are ‘one way’ valves for current
- Transistors are made with 3 layers of material, 2 layers for diodes
- Cathodes are commonly marked with a stripe

---
Semiconductors
- Field Effect Transistors (FET) are a special class
- Anode and Cathode are the ends of a diode
- Gain is a way of measuring amplification

---
Diagrams and Schematics
A diagram using a standard set of symbols is called a schematic

---
Schematic Symbols
A dark bar is often same as a regular bar. This is just
another example of an NPN transistor
        Transistors
PNP NPN
     NPN - “Not Pointing In”
A Lamp symbol
Potentiometer
variable resistor
As seen, a DC power supply. In some circles, the number of plates shown may indicate voltage. 1.5v per pair.
An electrolytic capacitor - polarized. Normal capacitors have parallel straight lines
Light Emitting Diode (LED)

---
Schematic Symbols
A transformer - a type of ‘stacked’ inductor. Left coil and right coil separated by an ‘inductive’ material - often steel
A variable inductor. Notice the inductor ‘humps’ and the wiper. Wiper is same as a variable resistor. Round humps = inductor
Variable capacitor
no wiper
An antenna
Ground

---
A basic schematic

---
Bit more complicated

---
The Device itself

---
Component Functions
Converting AC to DC is called ‘Rectification’ and is done by a rectifier.

---
Types of Switches

---
A Relay
Schematic of a common relay, used to switch high current using a low current control signal

---
Volt/Ohm Meter

---
Multimeter - Digital vs Analog
- Analog
  - Faster response
  - May be more precise
  - Delicate, easy to damage
- Digital
  - More flexible
  - May not show rapid changes
  - Often have more functions (frequency count, thermometer, etc)

---
“Tuned” circuit
- A circuit is said to be resonant when that circuit’s inductance and capacitance (magnetic and electrical fields) match the signal.
- In Radio, resonance and manipulation of its properties is important and useful.
- RF filters are made with inductors and capacitors They’ll impede certain frequencies and allow others.

---
Subelement 7, Station Equipment
- Receivers
- Transmitters
- Transceivers
- Modulation
- Transverters
- Transmit and receive amplifiers

---
Receiving signals
- Receivers must have a certain amount of signal
- More sensitive receivers require less signal
- Received signal can be improved by higher gain
  - Gain can be accomplished with antenna
  - Gain can be amplified
- Amplification will also increase noise
- Higher gain antenna, being frequency sensitive, may avoid or ignore noise

---
What is this stuff?
- Transceiver
  - Both receiver and transmitter in one device
- Sensitivity is ability to receive a signal
- Selectivity is ability to select a particular signal
- Oscillators generate specific frequencies
- Transverters convert RF to another band
- Activating a Push to Talk (PTT) button switches from receive to transmit

---
More terms
- Combining information (voice, data) onto an RF signal, no matter how, is called modulation
- Transmission amplifiers must switched to the correct mode (SSB/CW-FM). Some are auto detecting, many are not.
- Preamplifiers are used for received signals and go between the antenna and the receiver

---
Common problems
- A residential receiver with inadequate selectivity may accidentally receive amateur transmissions.
- Interfearence has many forms
  - Fundamental overload (STRONG signal on frequency)
  - Harmonics (adjacent frequencies ‘appear’ that aren’t transmitted
  - Spurious emmisions (many transmitters are ‘dirty’
- RF filters can reduce interference

---
Complaints of interference
- Ensure your station is operating correctly
- Test with your own receivers (TV, broadcast radio)
- Install ‘band pass’ filters to prevent harmonics or spurious emmisions
- You can prevent broadcast signals in your VHF receiver with a “Band-reject” filter tuned to the broadcast band

---
Unlicensed interference
- Someone else’s consumer equipment is causing you problems. Often noise
- Must work with the neighbor - be polite, accusations and finger pointing prevent progress
- Educate them on how the FCC rules work. They may not cause interference to licensed spectrum and are liable for their interference
- Ensure you’re doing things right, first!

---
Part 15 Devices
- Part 15 is a section of the FCC rules covers electronic devices
- Part 15 devices are NOT licensed, but may emit low levels of signal on licensed frequencies
- There are mandated limits
- Yes, you are protected, they are not. They must fix the problem. But, you’ve an obligation to help, guide and support their efforts the be betterment of all.

---
Signal Reports
- A great way to know if your station is operating correctly
- Bad audio on receive can be an indication of a problem
  - off frequency
  - lower battery/power supply
  - poor location (distance or angle)
  - poorly installed connectors
  - RF Feedback can create problems as well

---
Antenna measurements
- Dummy loads should be used when performing transmitter tests that don’t test your antenna
- An antenna analyzer can tell you on what frequencies your antenna system is resonant
- SWR is an indicator of how well a load is matched to a transmission line. 1:1 is a perfect match and is rarely achieved. 4:1 is an obvious impedance mismatch
- Modern, solid state transmitters will ‘fold back’ output power to protect themselves if there’s a bad match
- Poor matches waste energy as heat

---
What is an SWR meter?
- Basically, two directional watt meters in the same box
- Measures forward power from transmitter to antenna
- Measures reflected power back from the antenna
- Ratio of forward to reflected are the ratio
- It changed?? Moisture in cable is a common cause

---
Environmental consideratins
- Sunlight (UV) degrades many plastics
- If exposed, use outdoor rated coax with UV protection
- Ensure your cable is protected from moisture
  - Connectors must be weather rated
  - installed correctly
  - Jacket and protection must be in good shape
  - Foam core can prevent moisture ingress
  - Air core cable requires special handling

---
Basic repair and testing
- Soldering
- Using test instruments
  - Voltmeter
  - Ammeter
  - Ohmmeter

---
What do they measure?
- Voltmeter
  - Passive device measures voltage
  - Always used in parallel
- Ammeter
  - Passive device measures current
  - Always used in series
- Ohmmeter
  - Active device measures resistance

---
Test instruments - damage
- Most voltmeters will die due to
  - Wrong settings
  - Over voltage
  - Too high a current
- Using acid core (plumbers) solder or flux will damage equipment. Never use
- Cold solder joings look grainy and dull. Are poor connections and can create other problems

---
Ohmmeters
- Best used on components out of a circuit
- Has it’s own power supply - why it’s considered an ‘active’ device
- Capacitors in a circuit can charge up and affect readings, increasing resistance over time
- NEVER test on powered circuits with an ohmmeter!
- Always use correctly rated leads and meters on powered circuits

---
Amateur Radio – Technician Class Subelement 6 & 7
1. Tate Belden – KA7O
2. ka7o@casperarc.net
3. Casper Amateur Radio Club – W7VNJ
4. http://casperarc.net
5. Released under a Creative Commons Attribution-NonCommercial 4.0 International License. http://creativecommons.org/licenses/by-nc/4.0/