Radio Waves & Basic Electrical Concepts
The “Over the air” Part
Radio Wave Propagation (T3A, T3B, T3C):
  - Radio waves are electromagnetic; travel at speed of light (300,000,000 meters/sec).
  - Frequency: Cycles per second (Hertz - Hz).
    Higher frequency = shorter wavelength (shorter band).
    - Radio is closer to the lower end of the EM spectrum, lower frequency, longer wavelength
  - Wavelength Formula: λ =Frequency ÷ 300 [ λ in Meters, Freq in Mhz]​
    - Wavelength is ‘band’: 28–29.7Mhz 10meters, 50-54Mhz 6meters, 144-148Mhz 2meters, 420-450Mhz is 70cm, etc
  - VHF/UHF Propagation (primarily):
    - Line-of-sight (antenna height is important).
    - Can be reflected by surfaces, diffracted around objects.
    - Multipath can cause fading.
    - Tropospheric ducting can cause unusually long-distance VHF/UHF contacts (6m band is great, when it happens – “magic” band).
    - Absorption is a real concern at higher frequencies
      Vegetation, precipitation – water in atmosphere, special at microwave (2.4Ghz and up to about 5Ghz)
      - HF Propagation: Can use skywave (refraction off ionosphere 50 to 400 miles AGL) for long distances. Ionosphere height and strength strongly affected by solar activity.
      - Ionospheric strength determines Maximum Usable Frequency (MUF)
      - Ionosphere often has different layers, depending on time of day, season and solar activity. Different layers refract different bands
      - External events: meteors trails (6m), Aurora can affect EM refraction
  - EM Wave with E and M in phase is Linearly Polarized
  - Out of phase E and M is Circularly or Elliptically polarized, either L or R
              Cross/mis-matched polarization causes lower RX signal level
    - Refracting off Ionosphere changes polarization, so use an antenna that is physically manageable – it’ll work as well as any

The “In the wire” Part
- Basic Electrical Units (T5A):
  - Voltage (E or V): Electrical pressure. Unit: Volt (V).
  - Current (I): Flow of electrons. Unit: Ampere (A).
  - Resistance (R): Opposition to current. Unit: Ohm (Ω).
Ohm's Law (T5B): Relates Voltage, Current, and Resistance.
  - V = I × R
  - I = V ÷ R​
  - R = V ÷ I
- Electrical Power (P) (T5C): Rate of energy use. Unit: Watt (W).
  - P = I × V
  - I = P ÷ V
  - V = P ÷ I​
  - Decibels (dB): Ratio for power gain/loss.
    - +3 dB ≈ Power x 2
    - −3 dB ≈ Power x 1/2
    - +10 dB = Power x 10
    - -10 dB = Power x 1/10
- Current Types & Basic Circuits:
  - DC (Direct Current): Flows in one direction (e.g., batteries).
  - AC (Alternating Current): Reverses direction periodically (e.g., wall outlet).
  - Series Circuit: Single path for current. Current is same
  - Total Resistance equal sum of all resistances: Rtotal​=R1​+R2​+…
  - eg. 2 – 100 ohm resistors in series = 200 ohms resistance
  - Parallel Circuit: Multiple paths.
  - Voltage is same across branches.
  - Total resistance is less than smallest resistance
  - 1÷Rt = 1÷R1 + 1÷R2 + 1÷R3 + 1÷Rn
  - eg, 2 – 100 ohm resistors in parallel
    1÷Rt=(1÷100)+(1÷100)
          Rt=0.01+0.01
- 1÷0.02 = 50 ohms
- Prefixes:
    Megahertz and Kilohertz Relationship
    Zetta Z - Sextillion 10^21
    Exa E - quintillion 10^18
    Peta P - quadrillion 10^15
    Tera T - Trillion 10^12
    Giga G - Billion 10^9
    Mega M - Million 10^6
    Kilo k - Thousand 10^3
    Hecto - hundred
    Deka - tens
    1
    Deci d - Tenth 10^-1
    Centi c - Hundredth 10^-2
    Milli m - Thousandth 10^-3
    Micro μ - Millionth 10^-6
    Nano n - Billionth 10^-9
    Pico p - Trillionth 10^-12
    Femto f - Quadrillionth 10^-15

The relationship between megahertz (MHz), kilohertz (kHz), and hertz (Hz) is based on the metric system, where each unit represents a different scale of frequency measurement.
One hertz (Hz) is the base unit of frequency, representing one cycle per second.
A kilohertz (kHz) is equal to 1,000 hertz, meaning it represents 1,000 cycles per second.
Conversely, a megahertz (MHz) is equal to 1,000,000 hertz, or 1,000 kilohertz.
This means that 1 MHz is equivalent to 1,000 kHz, and 1 kHz is equivalent to 0.001 MHz.
To convert between these units, you can use the following relationships:
To convert from kHz to MHz, divide the frequency value in kHz by 1,000.
To convert from MHz to kHz, multiply the frequency value in MHz by 1,000.
For example, a frequency of 5 MHz is equivalent to 5,000 kHz, and a frequency of 2,500 kHz is equivalent to 2.5 MHz.

- Capacitance – energy stored in electrical field (plates)
- Inductance – energy stored in magnetic field (coil)

References:
  - ARRL Ham Radio License Manual, Chapters on Radio Wave Propagation and Electrical Principles.
  - https://www.electronics-notes.com/articles/antennas-propagation/ionospheric/hf-propagation-basics.php
  - https://www.qsl.net/4x4xm/Books-and-Articles/Understanding-Propagation-WB5ANN.pdf