Technician Class Session-3
“Over the Air and IN the Wire”
Tate, KA7O – ka7o@casperarc.net

---
Subelements
- T3A: Radio wave characteristics
- T3B: VHF/UHF propagation
- T3C: Ionospheric propagation
- Skipping T4A T4B for now – we’ll get them later
- T5A: Electrical Units
- T5B: Math for Electronics
- T5C: Electrical Power
- T5D: Ohm’s Law

---
Radio wave characteristics
- How a radio signal travels
- Fading
- Multipath (picket fencing)
- Polarization
- wavelength
- Absorption
- Antenna orientation
T3A: Radio wave characteristics
[Speaker Notes: We’re getting into the “Art” as well as the “Science” that is Radio]

---
Before we look at How, lets talk what
- Radio waves are a form of electromagnetic radiation
  - Like Light or X-rays
  - Travel at speed of light 186,000 miles/second
- Different frequencies and wavelengths
    - A cycle is a complete wave, meets zero line 3 times
  - Frequency measured in cycles per second, Hertz (Hz)
  - Kilohertz
  - Megahertz
  - Gigahertz
  - Terahertz

---
The Electromagnetic Spectrum

---
Notation
- 100,000,000,000,000,000,000 hertz
    - (the range of Gama/Cosmic Radiations)
- Sextillion, Quentillion, Quadrillion,Trillion, Billion, Million, Thousands
- 100 Exahertz
These numbers rapidly become too large to manage,
      let alone say – so, we ‘cheat’
- 100,000,000,000,000,000,000 == 10²⁰ == 10^20
  - 1 with 20 zeros behind it

---
Prefixes to show magnitude
- Zetta Z - Sextillion 10^21
- Exa E - quintillion 10^18
- Peta P - quadrillion 10^15
- Tera T - Trillion 10^12
- Giga G - Billion 10^9
- Mega M - Million 10^6
- Kilo k - Thousand 10^3

---
Frequencies in Radio
- Terahertz
  - Trillions of cycles per second (Getting in the range of visible light)
- Gigahertz
  - Billions of cycles per second
- Megahertz
  - Millions of cycles per second
- Hertz
  - Cycles per second

---
First, what is Frequency

---
Frequencies can be higher or lower
Never “faster” – always speed of light

---
Where in the spectrum are we?
- Radio is down low
  - Hertz, Kilohertz, Megahertz
- Visible light is sort of in the middle
  - Terahertz
- Dangerous radiations are up high
  - Petahertz, Exahertz, Zetahertz
- HF – 3 to 30Mhz
- VHF – 30 to 300Mhz
- UHV – 300 – 3000Mhz (3Ghz)

---
[Speaker Notes: This is a ‘nice’ chart of the EM Spectrum You’ll see these in many electronics oriented spaces]

---
Amateur Radio Allocations

---
EM Propagation
- Wave?
- Particle?
- Quantum?
- Observation effects?
Really – no one know for sure how it self propagates, but they’re looking
Point being: This can QUICKLY devolve into an incredibly complex and esoteric debate on the nature of existence
We just use what works – for us and our needs

---
An Electromagnetic Wave
What we DO know
- ALL EM waves travel at the same speed in vacuum
- 186,000 Miles per Second
- 299,732,458 Meters per Second
  - 299.7x10^5
  - 299 million, 7 thousand kilometers meters per second
  - 299.7 megameters per second
- 299,732,458 Meters per Second is rounded up for all practical purposes
- 300,000,000 Meters per second for our uses

---
So, it propagates – What’s that?

---
Wavelength vs Distance traveled
- For a given amount of time, the distance traveled by any wave is always the same
- What’s different is the number of cycles that pass any one point
  - Depends on frequency (how frequent does it pass)
- How many cycles in a given time, gives you the distance between cycles

---
Wavelength
- Distance in space, a single wave travels in one complete cycle
  - Measured in kilometers, meters, centimeters, millimeters

---
Wavelength
Higher Frequency = Shorter Wavelength
Lower Frequency = Longer Wavelength

---
The Bands – in meters
Take Velocity ‘V’ and divide by frequency ‘f’ to get wavelength

---
V/UHF Bands
- 144 – 148 Mhz
  - Split the difference, lets call it 146 Mhz
  - 300,000,000 ÷ 144,000,000 = 2.083333333 meters
  - Rounded out to “Two Meter Band”
  - Speed of light divided by frequency = wavelength in meters
- 420 – 450 Mhz
  - 300,000,000 ÷ 435,000,000 = 0.689655172 meter
  - Rounded out to “Seventy Centimeter Band”
  - Speed of light divided by frequency = wavelength in meters

---
So, why do we care about wavelength?
- Important for effective antennas
- Wavelength determines the effective electrical lengths of an antenna for any given frequency
- Different Wavelengths interact with the ionosphere differently
  - V/UHF ‘punch through’
  - HF refracts/reflects
Oh, one more thing…

---
Polarization
- If the E filed and M field are in phase (cross zero at same time) they are called “Linearly Polarized”
- If E field is vertical, said to be “Vertically Polarized”, uses Vertical antenna
- If E field is horizontal, said to be “Horizontally Polarized”, uses Horizontal antenna
- If the E field is out of phase with the M field called “Circular Polarization”, can be to the Right Circular (as seen from the TX antenna) or Left Circular – if uneven amplitude, it’s ‘elliptical’
- Use whatever antenna you can get in the air or specialized if weak signals (satellites, etc)

---
In phase - Linear

---
Out of Phase - Circular

---
Polarization
- Pretty much all you need to know is that different polarizations exist
  differences will affect RX signal level
- Horizontal is traditionally used for Long Distances (CW and SSB)
  - HF antennas are physically bigger and Horizontal are mechanically easier to build and deploy
  - CW and SSB on the V/UHF bands tend to follow that tradition
- For best results in radio – TX polarity should match RX polarity
- If they don’t, you’ll loose about half of your signal strength
- Interactions with Ionosphere can change polarization
- Effects may be rapid and dynamic, resulting a a ‘fluttery’ signal
  - Often caused by Aurora Effects, “Aural Flutter or Backscatter”

---
V/UHF Bands
- All EM radiation, travels in a straight line
- VHF and higher tends to ‘punch through’ the Ionosphere and not refract (shorter wavelengths)
- These frequencies are Called “Line of Sight”
- Just like vision, V/UHF radio can not ‘See’ around or through things
- If your signal can’t ‘see’ the other antenna due to obstruction (hills, buildings, curve of the earth) – they won’t receive you, no matter power, brand or mode
- (Note: for radio, the ‘horizon’ is slightly further than what is visible to the eye due to effects of the atmosphere on signals)

---
Antenna Height above ground is the winner!

---
Radio Signal Behaviors
- Reflection: can bounce off conductive surfaces or plasma (such as on 6m (best) or 2m meter tails, called meteor scatter)
- Diffraction: can ‘bend’ around edges of sharp obstacles
- Multipath: Signals arrive at the receiver via different paths
  - Can cause ‘picket fencing’, a rapid flutter, special when mobile
- Tropospheric Ducting (also Sporadic E):
  - Under certain conditions (such as a temp inversion) VHF (10, 6 and 2m) signals can be ‘ducted’ in the troposphere (lower atmosphere) hundreds or even thousands of miles
  - Tropoducting is way cool, but far from an everyday occurrence

---
Absorption
- Somethings block radio signals (radio opaque)
- Somethings allow radio signals to pass through (radio translucent)
- Most things can either block or allow, depending on the frequency of the signal
- V/UHF can be blocked by:
  - Vegetation
  - Precipitation
- UHF and Microwave frequencies are known to be easily blocked by Vegetation and Precipitation
- Lower frequencies (HF - 30Mhz - and below) are not strongly affected by Vegetation or Precipitation

---
The Ionosphere
- Tech class has limited HF privileges, but does have some
- The Ionosphere is a region of upper atmosphere (50 to 400 miles) ionized by the sun
  - Ionosphere heavily affected by solar activity (spots, flares, etc)
- HF signals (lower frequencies, longer wavelengths) can be refracted back to the earth by the ionosphere
  - Called “Skywave” or “Skip” propagation, can skip more than once
  - Allows for worldwide communication
- Refracted signals are often ‘circularly’ or ‘elliptically’ polarized
  - In such cases, Vertical or Horizontal antennas are often used

---
Ionospheric Skywave

---
Maximum Usable Frequency (MUF)

---
Different Ion layers – like a cake
And they change – time, season, sun activity, and more

---
Time of Day – Solar Conditions - frequency
Plus Aurora, meteor trails, etc will have an affect on propagation
Such as using 6m or 10m from dawn to shortly after sunset when sunspot activity is high to take advantage of strong F region effects
Understanding the affect of solar activity, sunspots, solar wind, flares, etc are part of the Science of Radio
Learning when to use what frequency to achieve desired communications is part of the Art of Radio

---
Break Time!
- 10 minutes
- Get up – walk a bit
- Get a drink
Be back here in 10 minutes and we’ll dive back in
That was mostly theoretical, now It’s beginning to get practical

---
The “In the Wire” stuff

---
Two types of Current
- Direct Current (DC) – flows in only one direction, like from a battery
  - No frequency, steady state
- Alternating Current (AC) – Current periodically reverses direction, like from a walls socket
  - Has a frequency, like an EM wave, but usually MUCH lower

---
Conductors and Insulators
- Anything that easily carries current is a Conductor
  - has lots of free electrons
  - Such as metal wire
  - Some liquids
- Anything that blocks a current is an Insulator
  - Glass (one of the best!)
  - Paper / wood (if dry)
  - Many Plastics

---
What is a circuit?
A circuit is a closed loop through which electricity can flow, allowing electrons to move from a power source, through various components, and back to the source.

---
Language of Electricity
Think of Electricity in a wire as similar to water in a pipe
- Voltage: Volts (V or E) – Electromotive Force, Pressure, like water in a pipe
- Current: Amps (A or I) - The quantity of electrons moving past a point, kind of like ‘gallons’ of water in a pipe
- Resistance: Ohms (Ω) - Opposition to current flow, like friction or a narrow section in a pipe
(be aware, the ‘pipe’ analogy is handy, but doesn’t work for all things)

---
What?
A instead of I except before E or V?
- E = Electromotive Force
  - Measured in Volts
  - V = Volts
- I = from the French phrase intensité du courant (current intensity)
  - The ‘I’ symbol was used by André-Marie Ampère
  - Now we ‘simplify’ to A for Amps
- Volts = V or E
- Amperage = A or I
  No rules on usage – use what’s comfortable for you

---
Welcome to Ohm’s Law
- One of - if not the - most important ‘law’ or ‘rule’ to understand electricity
- Describes the relationship(s) between:
  - Voltage
  - Amperage
  - Resistance
  - Power
- How all this works together

---
A ‘picture’ of Ohms Law

---
Ohms Law
- Ohm’s Law is defined as: Voltage = Current times Resistance
  - V=IxR (often seen as V=IR)
- Can be re-arranged to solve for any missing variable
- Current = Voltage divided by Resistance
  - A=I÷R (often seen as A=I/R)
- Resistance = Voltage divided by Current
  - R = V÷I (or R=V/I)
V = Voltage, I = Amperage, R = Resistance in Ohms

---
Electrical math
- We only need the basics
- Multiplication (side by side)
- Division (one over the other)
- Variables (v=Volts, I=Amps, R=Ohms, P=Watts)
- Remember:
  - V over I by R or “VIR”

---
Triangles help - VIR

---
Cover what’s missing

---
Practice
A 12 Volt Circuit with a resistance of 6 Ohms, what is the current?
[Speaker Notes: 12 / 6 = 2]

---
Practice #2
If 3 Amps flow through a 4 Ohm resistor, what is the voltage across that resistor?
[Speaker Notes: 3 * 4 = 12]

---
Power
- Power: Watts – rate at which work is done. Rate of electrical energy being converted or consumed (like heat or radio waves)
- Basic Power Formula: P = I x V
  - Power = Current multiplied by Voltage
- Can also be rearranged to find missing value
- Remember
  - P over I by V or “PIV”

---
Power Triangle - PIV

---
Used the same way

---
That’s it
That’s it for Ohm’s Law
Simple idea – lots of questions
Once you’ve got that, you’ve the tools for understanding the relationships of these ‘effects’
No need to over complicate things – will be used a lot

---
Ratios, expressed
Decibels (dB): A way to express ratios, used for signal strength, power, gain, or losses – Is Logarithmic
  - +3dB = Power approximately Doubles
  - -3dB = Power approximately Halves
  - +10dB = Power increases 10 times
  - -10dB = power reduces to 1/10th
 hint: divide dB by 3 - 12dB is (12÷3=4) so 4 doublings
     5 watts into +12dB = (10, 20, 40, 80) 80 watts

---
Series Circuit
- Components are connected end to end, forming a single path for the current
  - Current is the SAME through all components
  - Total resistance is the SUM of all individual resistances
  - If one component breaks, the entire circuit stops working

---
Series Circuit

---
Parallel Circuit
- Components are connected side-by-side, providing multiple paths for current
  - Voltage is the SAME across all components
  - Total resistance is less than the smallest individual resistance
  - If one component breaks, other branches can still operate
- Total Resistance is always less than any individual Resistance in the circuit
  - eg. 2 - 100ohm resistors in parallel offer 50ohms of resistance

---
Parallel Circuit

---
Capacitance and Inductance
- Capacitance: Ability to store energy in an electrical field
  - Measured in Farads
- Inductance: Ability to store energy in a magnetic field
  - Measured in Hennries
- Impedance: An opposition to AC current flow
  - Measured in Ohms (similar to, but not same as resistance)

---
Capacitor
Stores energy as an electrical field between plates

---
Inductor
Stores energy as a magnetic field in a coil

---
Impedance
- Not really a good visualization available
- Used to describe suitability of antennas, filters, chokes, etc for a given transmitter
- Most ham gear is 50Ohm impedance
- Uses 50Ohm Feedlines, filters, chokes and antennas
- Allows for most efficient transmission of power from transmitter to antenna
- Mismatched Impedances will reflect energy back to transmitter, can cause damage (The whole vSWR dance is in here)

---
OK - We’re done for today – Congrats!
- Ohm’s Law and Power Formula are CRITICAL
  - Get those down cold
- Use the visuals so you know how to structure your formulas
- Pay attention to prefixes and their decimal equivalents
  - Surprising how many “Kilo” to Mega to hertz questions there are
Have a great week! Any questions – holler
Tate – KA7O, ka7o@casperarc.net