T3A T3B
T5A T5B T5C T5D
How Radio Waves Travel & Basic Electrical Concepts
- Time Allotment: 60 minutes instruction, 30 minutes Q&A/Discussion
- Learning Objectives:
  - Understand basic radio wave characteristics (frequency, wavelength).
  - Describe common VHF/UHF propagation modes (line-of-sight, reflection, etc.).
  - Define fundamental electrical units: voltage, current, resistance, power.
  - Understand Ohm's Law and the power formula (P=IE).
Materials Needed (Teacher's Note):
  - Whiteboard or projector.
  - Handout 3.
  - Optional: Simple props to demonstrate line-of-sight (e.g., two small objects and a string or laser pointer). A 9V battery, small lightbulb (with holder), and wires to demonstrate a simple circuit.
Key Topics Covered (Corresponds to Subelements T3A, T3B, T3C, T5A, T5B, T5C):
  - Subelement T3A: (12) Radio wave characteristics: frequency, wavelength, velocity. Relationship between frequency and wavelength.
  - Subelement T3B: (11) VHF/UHF propagation: line-of-sight, reflection, refraction, diffraction, multipath, tropospheric ducting.
  - Subelement T3C: (11) Ionospheric propagation (briefly, as it's more relevant to HF but good for context), skip, solar activity effects.
  - Subelement T5A: (12) Electrical units: volt (V), ampere (A), ohm (Ω).
  - Subelement T5B: Math for Electronics: Conversin of units, decibels
  - Subelement T5C: (13) Electrical power (P=I×E), decibels (dB) as a measure of relative power.
  - Subelement T5B: (13) Ohm's Law (E=I×R).
Teacher's Script (Outline & Key Points):
(0-20 min) Radio Waves on the Move (Subelements T3A, T3B, T3C)
- "We've talked about rules and operating. But how do our signals actually get from Radio A to Radio B? It's all about radio waves."
- Subelement T3A: Radio Wave Characteristics
  - Radio waves are a form of electromagnetic radiation, like light or X-rays, but with different frequencies and wavelengths. They travel at the speed of light (approx. 300 million meters/second or 186,000 miles/second).
  - Frequency: Number of cycles per second. Measured in Hertz (Hz).
    - Kilohertz (kHz) = thousands of Hz
    - Megahertz (MHz) = millions of Hz (common for VHF/UHF)
    - Gigahertz (GHz) = billions of Hz
  - Wavelength: Distance a wave travels in one complete cycle. Measured in meters, centimeters.
  - Relationship: Wavelength and frequency are inversely related.
    - Higher frequency = Shorter wavelength.
    - Lower frequency = Longer wavelength.
    - Formula: λ (wavelength in meters)=f (frequency in MHz)300​. (Good to know concept, not critical to memorize formula for exam, but helps understand antenna sizes).
Subelement T3B: How VHF/UHF Signals (Mostly) Travel
  - Line-of-Sight: For VHF/UHF bands (where Technicians have most privileges), signals primarily travel in a straight line.
    - If you can't "see" the other antenna due to obstructions (hills, buildings), communication is difficult or impossible. (Use props to demonstrate).
    - The "radio horizon" is slightly farther than the visual horizon due to some atmospheric bending.
    - Antenna height is key for increasing line-of-sight range.
  - Reflection: Signals can bounce off conductive surfaces like buildings, airplanes, sometimes even dense foliage.
  - Diffraction: Signals can bend around the edges of sharp obstacles.
  - Multipath: Signals arrive at the receiver via multiple paths (direct, reflected). This can cause fading or "picket fencing" (fluttering sound) especially when mobile.
  - Tropospheric Ducting/Bending: Under certain weather conditions (e.g., temperature inversions), VHF/UHF signals can be ducted or bent in the troposphere (lower atmosphere) and travel hundreds, even thousands, of miles! These are exciting but not everyday occurrences.
Subelement T3C: A Glimpse at HF Propagation (Ionosphere)
  - "While Technicians have limited HF privileges, it's good to understand how long-distance HF communication happens."
  - The ionosphere is a region of Earth's upper atmosphere (50-400 miles up), ionized by solar radiation.
  - HF signals (lower frequencies, longer wavelengths) can be refracted (bent) back to Earth by layers in the ionosphere. This is called skywave propagation or "skip." This allows for worldwide communication.
  - The ionosphere's condition is heavily affected by solar activity (sunspots, solar flares). More sunspots generally mean better HF propagation.
Historical Anecdote: "Guglielmo Marconi's famous 1901 transatlantic transmission was a landmark. Many scientists at the time didn't believe it was possible for radio waves to follow the Earth's curvature over such a distance. They didn't fully understand the ionosphere yet. This event spurred much research into how radio waves propagate, leading to the understanding of 'skip' that hams use every day for global contacts."
(20-45 min) The Language of Electricity (Subelements T5A, T5B, T5C)
- "To understand our radios, we need to grasp some basic electrical concepts. Think of electricity flowing like water in a pipe – it's a helpful analogy."
- Subelement T5A: Fundamental Electrical Units
  - Voltage (E or V): Electrical "pressure" or potential difference. Like water pressure in a pipe.
    - Unit: Volt (V). Named after Alessandro Volta.
  - Current (I): Flow of electrons. Like the rate of water flow (gallons per minute).
    - Unit: Ampere (A or amp). Named after André-Marie Ampère.
  - Resistance (R): Opposition to current flow. Like friction or a narrow section in a pipe.
    - Unit: Ohm (Ω). Named after Georg Ohm.
Subelement T5B: Ohm's Law – The Fundamental Relationship
  - "This is arguably the most important formula in basic electronics. It beautifully describes the relationship between Voltage, Current, and Resistance."
  - E=I×R (Voltage = Current multiplied by Resistance)
  - It can be rearranged to solve for any variable:
    - I=RE​ (Current = Voltage divided by Resistance)
    - R=IE​ (Resistance = Voltage divided by Current)
  - (Draw the Ohm's Law triangle on the board: E on top, I and R on the bottom. Cover the one you want to find).
  - Practice simple examples:
    - "If a circuit has 12 Volts applied and a resistance of 6 Ohms, what is the current?" (I=6Ω12V​=2A).
    - "If 3 Amps flow through a 4 Ohm resistor, what is the voltage across it?" (E=3A×4Ω=12V).
Subelement T5C: Electrical Power (P)
  - Power: The rate at which electrical energy is converted to another form (like heat or radio waves) or consumed.
    - Unit: Watt (W). Named after James Watt.
  - Basic Power Formula: P=I×E (Power = Current multiplied by Voltage)
  - Using Ohm's Law, we can also derive: P=I2×R and P=RE2​. (These are useful for exam questions).
  - Practice simple examples:
    - "If a radio draws 2 Amps from a 12 Volt supply, how much power does it consume?" (P=2A×12V=24W).
    - "If a 100 Watt transmitter is fed by a 12 Volt supply, how much current does it draw (ideally)?" (I=EP​=12V100W​≈8.33A).
  - Decibels (dB): A way to express ratios, often used for signal strength, power gain, or loss. It's logarithmic.
    - +3 dB = Power approximately doubles.
    - −3 dB = Power approximately halves.
    - +10 dB = Power increases 10 times.
    - −10 dB = Power reduces to 1/10th.
    - Important for understanding antenna gain and feed line loss (which we'll cover later).
(45-55 min) Direct Current (DC) vs. Alternating Current (AC) & Basic Circuits (Brief Overview)
- Direct Current (DC): Current flows in one direction only (e.g., from a battery).
- Alternating Current (AC): Current periodically reverses direction (e.g., household electricity).
- Series Circuit: Components are connected end-to-end, forming a single path for current.
  - Current is the SAME through all components.
  - Total resistance is the SUM of individual resistances (Rtotal​=R1​+R2​+...).
  - If one component breaks (open circuit), the entire circuit stops working (like old-style string Christmas lights).
Parallel Circuit: Components are connected side-by-side, providing multiple paths for current.
  - Voltage is the SAME across all components.
  - Total resistance is less than the smallest individual resistance.
  - If one component (on one branch) breaks, other branches can still operate (like household wiring).
  - (The formula for parallel resistance is 1/Rtotal​=1/R1​+1/R2​+..., or for two resistors: Rtotal​=(R1​×R2​)/(R1​+R2​). Focus on the concept that total R is less).
(55-60 min) Wrap-up for Instruction & Preview Next Session
- "We've covered how signals travel and the very basics of electricity – voltage, current, resistance, and power. These are the foundational building blocks for understanding radio."
- "Next time, we'll look at the specific electronic components that use these principles, like resistors, capacitors, and inductors, and how they are represented in diagrams."
(60-90 min) Q&A and Discussion
- Work through more Ohm's Law and power calculation examples if students need them. Use simple numbers.
- Use the water analogy frequently to clarify voltage, current, and resistance.
- If you have a battery and bulb, demonstrate a simple series circuit.
Teacher's Notes (Session 3):
- Ohm's Law and Power Formula are CRITICAL. Spend enough time here. The triangle aids are very helpful for visual learners. Write out all steps for examples.
- Math anxiety: For the 55+ group, some may be uncomfortable with formulas. Reassure them that the math is simple algebra and the exam uses straightforward numbers. Focus on understanding the concepts and how to use the formulas.
- Abstract concepts: Electron flow can be tricky. Stick to analogies.
- Ionosphere discussion: Keep it brief and conceptual for Technicians. Their main focus is VHF/UHF line-of-sight.
- Visuals: Simple diagrams of wave propagation, series/parallel circuits are very effective.

Q&A Discussion Prompts (Session 3):
- "If you want to talk further on VHF, what's one simple thing you can do to improve your signal's reach?" (Increase antenna height).
- "Let's try an Ohm's Law problem: If your car radio uses 5 Amps from your 12-Volt battery, what's the equivalent resistance of the radio?" (R=5A12V​=2.4Ω).
- "Why might a signal from a mobile station fade in and out as it moves?" (Multipath).