Student Handout 4: Building Blocks of Electronics: Components & Circuits
Passive Components (Store or dissipate energy):
  - Resistor (T6A): Opposes current. Unit: Ohm (Ω).
    - Symbol: Zigzag line (US) or rectangle (Int'l). Arrow for variable (potentiometer).
    - Power rating in Watts.
  - Capacitor (T6A): Stores energy in an electric field; blocks DC, passes AC. Unit: Farad (F) ( μF,nF,pF).
    - Symbol: Two parallel lines (non-polarized); one straight, one curved (polarized). Arrow for variable.
    - Polarized capacitors (e.g., electrolytic) must be connected with correct polarity (+/-).
  - Inductor (Coil) (T6B): Stores energy in a magnetic field; opposes changes in current; passes DC, resists AC. Unit: Henry (H) (mH, μH).
    - Symbol: Series of loops/coils. Lines above for iron/ferrite core. Arrow for variable.
  - Transformer (T6B): Transfers AC energy between circuits, often changing voltage/current levels (step-up/step-down).
    - Symbol: Two coils separated by lines (representing core).
Active Components (Control electron flow; often require power to operate):
  - Diode (T6C): Allows current flow in ONE direction only (Anode to Cathode).
    - Symbol: Triangle pointing to a line →∣.
  - LED (Light Emitting Diode) (T6C): Diode that emits light. Requires current-limiting resistor.
    - Symbol: Diode symbol with arrows indicating light.
  - Transistor (BJT) (T6C): Amplifies signals or acts as an electronic switch. Terminals: Base, Collector, Emitter.
    - Types: NPN, PNP (symbols differ by arrow on emitter).
Integrated Circuit (IC) (T6D): Complex circuit on a single chip (e.g., microprocessor, voltage regulator).
  - Symbol: Often a rectangle with numbered pins.
- Schematic Diagrams (T6D): Roadmaps of electronic circuits using component symbols.
- Basic Test Equipment (Multimeter Functions) (T7D):
  - Voltmeter: Measures Voltage (connect in PARALLEL, power ON).
  - Ammeter: Measures Current (connect in SERIES, power ON – break circuit).
  - Ohmmeter: Measures Resistance (connect across component, POWER OFF).
References:
  - ARRL Ham Radio License Manual, Chapters on Components and Circuits.
  - Online schematic symbol charts.
  - https://www.ariat-tech.com/blog/comprehensive-guide-to-variable-resistor-symbol.html
  - https://www.jotrin.com/technology/details/capacitor-symbol
  - https://learn.sparkfun.com/tutorials/light-emitting-diodes-leds/introduction
  - https://www.allaboutcircuits.com/textbook/alternating-current/chpt-9/step-up-and-step-down-transformers/
  - https://quizlet.com/301421196/ham-radio-technician-questions-till-2022-set-t6c-diagram/
  - https://docs.onion.io/omega2-maker-kit/circuit-diagram-crash-course.html