Session - 4
Tate, KA7O
ka7o@casperarc.net

---
Subelements Covered
- T6A
    - Resistors (fixed, variable, briefly color code)
    - Capacitors (fixed, variable, units
    - Schematic Symbols
- T6B
    - Inductors (fixed, variable, cores)
    - Transformers (step-up/step-down)
    - Schematic symbols

---
Subelements Covered
- T6C
    - Diodes (Rectifier, LED
    - Transistors (NPN, PNP, BJT as switch/amplifier)
    - Schematic Symbols
- T6D
    - Integrated Circuits (ICs)
    - Basic Schematic reading

---
Subelements Covered
- T7D
    - Basic Test Equipment
    - Voltmeter
    - Ammeter
    - Ohmeter
    - Multimeter functions

---
Last Session into Today
- Last Session
  - Ohms Law and Watts
- Today
  - The physical parts – components – that make up circuits and follow these laws
  - Basics of what they do
  - Their Schematic symbols

---
Be aware
- Today’s stuff is quite basic
- Recognize symbols
- Recognize component function
  - e.g. what’s used to do what
- Familiar with one basic tool in two flavors
  - Be safe with things!

---
Two types of Components
- Passive
  - Do not require an external power source and cannot amplify signals
  - Include resistors, capacitors, inductors, and transformers
  - used for energy storage, filtering, and signal conditioning
- Active
  - Active components require an external power source to operate and can amplify or control the flow of current or voltage
  - transistors, diodes, and integrated circuits (ICs), which can provide power gain and control the flow of current or voltage

---
First passive is “Resistors”
- Function:
  - Oppose the flow of current (as learned with Ohm’s Law)
- Unit
  - Ohms - Ω

---
Resistor Types
- Fixed
  - Have a specific, unchanging value
  - Often marked with color bands to indicate value and tolerance
  - No need to memorize color code – not on the test
- Variable
  - Also called Potentiometers or Rheostats
    - Resistance can be changed with knob or slider
    - Often used for a volume control
      - Adjusts resistance into an output or speaker

---
Schematic Symbols for Resistors
Two Basic Types

---
Resistor in a circuit

---
Capacitors
- Function
  - Opposes changes in voltage
  - Store electrical energy in an electric field
  - Basic Structure: Conductive plates separated by an insulator
  - Block flow of DC, but allow AC (more easily at higher frequencies)
  - Unit – Farads – F
    - Practical units are
      - Microfarads μF (millionths)
      - Nanofarads nF (billionths)
      - Picofarads pF (trillionths)

---
Symbols
- Read the notes and verify types and specs
  - Some types are polarized
  - Reversing polarity can cause it to ‘pop’ or explode
- There really are more types, flavors, builds and packaging for capacitors than we’ve time to cover

---
Symbol – Fixed Capacitors

---
Symbols – Variable Capacitors

---
Inductor
- Inductance: Unit of Value: Henry – H
- Oppose changes in current
- Stores energy in a magnetic field
- Pass DC easily, but resist AC (more so at higher freqs)
- As current flows, a magnetic field is created
- When current drops, magnetic field collapses
- Collapse of the field induces current in the wire
- May have a core (iron or ferrite) to increase inductance

---
Inductor

---
Inductor - variable

---
Transformers
- Changes Voltage
  - Voltage down, amperage goes up
  - Voltage up, amperage goes down
  - Conservation of Energy and all that
- Essentially two inductors with a common core
- Step up or Step down have more ‘windings’ on one side than the other (isolators are the same on both sides)
- Ratio of windings from primary side to secondary side indicates if it’s a Step Up or a Step Down
  - Fewer on Secondary is Step Down
- Decreases Voltage, Increases Amperage
  - Power mostly stays the same (ignoring losses)
  - Only works with AC, does nothing with DC

---
Transformer – step down

---
Transformer – Step Up

---
Switches
- Simply open or close a circuit
- Ps and Ts
  - Poles and Throws
  - Pole – how many switching elements in play
  - SPST
  - Single Pole, Single Throw
  - Like a basic ‘On/Off’ switch

---
Switches and throws
- SPDT
  - Single Pole, Double Throw
- DPDT
  - Double Pole, Double Throw

---
Schematic

---
Fuses
- Function
  - Protect other components from current overload
- Unit
  - Amps – A
  - Fast, slow, delayed – many types
- Fuses are ‘self sacrificing’
  - They’ll fail open when current rating is exceed
- Breakers do the same thing, but can be reset and re-used

---
Fuse – in a circuit
Fuse, but fancier

---
Batteries
- Two basic types
  - Single use - disposable
    - Alkaline
    - Carbon Zinc
  - Multi use - Rechargeable
    - Nickle Metal Hydride
    - Lithium-ion
    - Lead Acid

---
Battery - schematic

---
Battery in a circuit

---
Diodes
- Allows current through in only one direction
- A voltage drop is involved (typical 1.5v)
- Some types have lower voltage drops others
- Light Emitting Diodes (LEDs) are a special type of diode
- Used to make Rectifiers (Bridges)
  - Change AC in to DC

---
Diode and LED

---
Transistors
- Function
  - Can act as an electronic switch (on or off)
  - Or as an amplifier
    - May be used in pairs for higher gain

---
Transistor Types
- Bipolar Junction
  - 3 terminals
    - Base, Collector and Emmiter
  - Small current or voltage at Base, controls a larger current flow between Collector and Emitter.

---
NPN and PNP types

---
Transistor
- Field Effect Transistor (FET)
  - Voltage Operated
  - 3 terminal device
    - Source (source of current)
    - Drain (current leaves)
    - Gate (controls flow)

---
FET Schematic
Don’t sweat FETs, not on the test

---
Relay
- An Electrically (not electronically) controlled switch
  - Use a small current to switch much larger current on or off
  - Comprised of an electromagnet and a magnetically operated switch
  - When electromagnet is powered, switch changes state
  - Can be Normally Open or Normally closed at rest

---
Integrated Circuits (ICs or Chips)
- Function
  - Contain many (sometimes millions) of transistors, diodes, resistors, and capacitors fabricated on a tiny single chip of semiconductor material. They perform complex functions.
- Many, many types, builds and packages

---
ICs
- Examples
  - Microprocessors (the "brain" of a computer), memory chips, operational amplifiers (op-amps), voltage regulators.
- Schematic symbol
  - Often a rectangle or square with numbered pins. The function is usually identified by a part number printed on it (7805, voltage regulator)

---
Schematics
- A ‘road map’ for an electronic circuit
- Uses standardized symbols to show components and how they’re connected
- Key is being able to recognize component symbols

---
ICs - Schematically
- Often just a labeled rectangle (or triangle)
  - Labels will indicate type (part number)
  - Pins

---
More symbols
Antennas

---
Ground

---
Many components used together
- e.g. An Inductor and a Capacitor can be used together to make a Resonant or Tank Circuit
  - A resonant circuit, also known as a tuned circuit or tank circuit, is an electrical circuit that combines an inductor (L) and a capacitor (C) to respond to a specific frequency. Like in some filters.
- LEDs and Resistors
  - Resistor acts as a ‘current’ limiter to avoid burning up an LED
- Diodes
  - Can be assembled into a ‘Rectifier Bridge’ to convert AC to DC

---
Basic Test Equipment
- Multimeter
  - Voltmeter - voltage
    - Connect in Parallel to measure voltage
  - Ammeter - current
    - Connect in Series to measure current
  - Ohmeter – resistance
    - POWER OFF!
    - Parallel to Device Under Test (DUT)

---
Multimeters can be...
- Analog
  - Uses a needle to sweep across a range
  - Often requires manual range selection
- Digital
  - Displays results as numbers
    - Often autoranging

---
DVM and AVM

---
That’s all for this one!
- Good luck and thanks for being here
- As always – any questions, holler!
Don’t forget the “Library” on the casperarc.net web page
Tate, KA7O
ka7o@casperarc.net