Building Blocks of Electronics: Components & Circuits
- Time Allotment: 60 minutes instruction, 30 minutes Q&A/Discussion
- Learning Objectives:
  - Identify common electronic components and their basic functions (resistors, capacitors, inductors, diodes, transistors, integrated circuits).
  - Recognize basic schematic symbols for these components.
  - Understand the function of basic test equipment.
Materials Needed (Teacher's Note):
  - Whiteboard or projector.
  - Handout 4.
  - Optional: A kit of common electronic components to show students (resistors with color bands, various capacitors, inductors, LEDs, transistors). A simple multimeter.
Key Topics Covered (Corresponds to Subelements T6A, T6B, T6C, T6D, T7D):
  - Subelement T6A: Resistors (fixed, variable, color code briefly), capacitors (fixed, variable, units). Schematic symbols.
  - Subelement T6B: Inductors (fixed, variable, cores), transformers (step-up/step-down). Schematic symbols.
  - Subelement T6C: Diodes (rectifier, LED), transistors (NPN, PNP BJT as switch/amplifier). Schematic symbols and basic function.
  - Subelement T6D: Integrated Circuits (ICs), basic circuit diagram (schematic) reading.
  - Subelement T7D: Basic test equipment: voltmeter, ammeter, ohmmeter (multimeter functions).
Teacher's Script (Outline & Key Points):
(0-20 min) Passive Components: The Resistors, Capacitors, and Inductors (Subelements T6A, T6B)
- "Last session, we learned about Ohms and Watts. Today, we'll look at the actual physical parts – components – that make up electronic circuits and follow these electrical laws."
- Subelement T6A: Resistors & Capacitors
  - Resistors:
    - Function: Oppose the flow of current (as we learned with Ohm's Law). Used to limit current, divide voltage, create heat (sometimes intentionally).
    - Unit: Ohms (Ω).
    - Types:
      - Fixed Resistors: Have a specific, unchanging resistance value. Often marked with color bands to indicate value and tolerance (briefly explain color bands are a system, but not critical to memorize for Technician exam – values usually given).
      - Variable Resistors (Potentiometers/Rheostats): Resistance can be changed, often with a knob or slider (e.g., volume control, light dimmer).
    - Schematic Symbol: (Draw zigzag line for fixed North American symbol, rectangle for international. Arrow through it or wiper for variable).
    - Power rating: How much power (heat) they can dissipate before being damaged.
  - Capacitors:
    - Function: Store electrical energy in an electric field (like a tiny, very temporary rechargeable battery). They block the flow of DC but allow AC to pass (more easily at higher frequencies).
    - Unit: Farads (F). Practical units are microfarads (μF, millionths), nanofarads (nF, billionths), and picofarads (pF, trillionths).
    - Types: Fixed, Variable (e.g., tuning capacitor in older radios).
    - Schematic Symbol: (Draw two parallel lines for basic non-polarized. One straight, one curved line for electrolytic/polarized. Arrow through it for variable).
    - Polarized Capacitors (e.g., electrolytic, tantalum): Must be installed correctly with regard to positive (+) and negative (-) terminals. Incorrect installation can cause them to be damaged or even explode!
Subelement T6B: Inductors & Transformers
  - Inductors (Coils):
    - Function: Store electrical energy in a magnetic field when current flows through them. They oppose changes in current. They pass DC easily but resist AC (more so at higher frequencies).
    - Unit: Henrys (H). Practical units are millihenrys (mH, thousandths) and microhenrys (μH, millionths).
    - Construction: Often a coil of wire, sometimes wound on a core material (like iron or ferrite) to increase inductance.
    - Schematic Symbol: (Draw a series of loops/coils. Parallel lines above/beside for an iron/ferrite core. Arrow for variable).
  - Transformers:
    - Function: Transfer electrical energy from one AC circuit to another via a shared magnetic field, often changing voltage and current levels. They do NOT work with DC.
    - Construction: Two or more coils (windings – primary and secondary) on a common core (usually iron).
    - Step-up Transformer: More turns on secondary than primary → increases voltage, decreases current.
    - Step-down Transformer: Fewer turns on secondary than primary → decreases voltage, increases current. (Power mostly stays the same, ignoring losses).
    - Schematic Symbol: (Draw two coils separated by parallel lines representing the iron core).
(20-35 min) Active Components: Semiconductors – Diodes & Transistors (Subelement T6C)
- "Now for components that can do more 'active' things like switch, rectify, or amplify – semiconductors."
- Diodes:
  - Function: Allow current to flow easily in ONE direction only. Like an electrical one-way valve or check valve.
  - The two terminals are called Anode (+) and Cathode (-). Conventional current flows from Anode to Cathode.
  - Uses: Rectification (converting AC to DC in power supplies), signal detection, circuit protection.
  - Schematic Symbol: (Draw triangle pointing to a line: →∣. Arrow indicates direction of conventional current flow).
  - LED (Light Emitting Diode): A special type of diode that gives off light when current flows through it in the forward direction. Requires a current-limiting resistor.
    - Schematic Symbol: (Diode symbol with little arrows pointing away from it, indicating light).
Transistors:
  - Function: Can act as an electronic switch (turning current on or off) or as an amplifier (making a weak signal stronger). The workhorse of modern electronics.
  - Types (focus on BJT for Technician):
    - BJT (Bipolar Junction Transistor): Has three terminals: Base, Collector, Emitter. A small current or voltage at the Base controls a larger current flow between Collector and Emitter.
      - NPN and PNP types: Differ in internal construction and voltage polarities.
      - Schematic Symbols: (Draw NPN and PNP symbols – circle with base line, collector/emitter lines angled. Arrow on emitter shows direction of conventional current. NPN: Arrow Not Pointing iN. PNP: Arrow Points iN Proudly).
    - FET (Field Effect Transistor): Another type, controlled by voltage. (Mention briefly, less emphasis for Tech).
Historical Anecdote: "The invention of the transistor at Bell Labs in 1947 by Bardeen, Brattain, and Shockley was a monumental leap. Before transistors, electronics relied on bulky, fragile, power-hungry vacuum tubes. Transistors made possible the miniaturization, efficiency, and reliability we see in everything from smartphones to the handheld radios many of you might use. It truly changed the world."
(35-45 min) Integrated Circuits (ICs) & Reading Schematics (Subelement T6D)
Integrated Circuits (ICs or Chips):
  - Function: Contain many (sometimes millions) of transistors, diodes, resistors, and capacitors fabricated on a tiny single chip of semiconductor material. They perform complex functions.
  - Examples: Microprocessors (the "brain" of a computer), memory chips, operational amplifiers (op-amps), voltage regulators.
  - Schematic Symbol: Often a rectangle or square with numbered pins. The function is usually identified by a part number printed on it (e.g., 741 op-amp, 7805 voltage regulator).
Circuit Diagrams (Schematics):
  - "A schematic is like a roadmap for an electronic circuit. It uses standard symbols to show which components are used and how they are interconnected."
  - (Show a very simple schematic, e.g., a battery, switch, resistor, and LED. Point out the symbols and trace the current path).
  - Being able to recognize basic component symbols is key.
(45-55 min) Checking Up: Basic Test Equipment (Subelement T7D)
- "To build, troubleshoot, or check our circuits and equipment, we use test instruments."
- Multimeter: A common, versatile handheld tool that combines several measurement functions.
  - Voltmeter: Measures voltage (electrical pressure).
    - How to connect: IN PARALLEL across the component or points where you want to measure voltage.
  - Ammeter: Measures current (electron flow).
    - How to connect: IN SERIES with the circuit – you have to break the circuit and insert the ammeter so current flows through it. (Caution: Incorrect connection, like across a voltage source, can damage the meter or circuit).
  - Ohmmeter: Measures resistance.
    - How to connect: Across the component being measured, WITH ALL POWER TO THE CIRCUIT TURNED OFF. Measuring resistance in a powered circuit can damage the meter or give false readings.
  - (If you have a multimeter, demonstrate selecting functions and how probes connect. Emphasize safety for ammeter/ohmmeter).
(55-60 min) Wrap-up for Instruction & Preview Next Session
- "We've now seen the key electronic building blocks and how they're drawn on schematics. Understanding their roles is important for appreciating how radios work and for any future tinkering you might do."
- "Next session, we'll put these components together in a conceptual way to look at actual station equipment like transceivers and power supplies, and explore how we put our voice or data onto radio waves using modulation."
(60-90 min) Q&A and Discussion
- Review schematic symbols if students are unsure. Use flashcard style if helpful.
- If you have physical components, pass them around (if safe and practical). Let students see the resistor color bands, capacitor markings, transistor shapes.
- Discuss any real-world examples of these components they might be familiar with (e.g., LED in a TV remote, potentiometer in a dimmer switch).
Teacher's Notes (Session 4):
- Visuals are key: This session is heavy on symbols and component identification. Use clear drawings and show real components if possible.
- Don't get bogged down in deep theory: For Technicians, it's about recognition and basic function, not designing circuits.
- For the 55+ group: Connect components to everyday items. The "water analogy" can still be useful for explaining what components do to the "flow."
- Safety with Multimeters: Clearly explain the difference in connecting voltmeters (parallel, circuit powered) vs. ammeters (series, circuit powered) vs. ohmmeters (parallel, circuit unpowered). This is a common point of error for beginners.
- Resistor Color Code: Mention it exists, perhaps show a chart, but reassure them it's not a major exam focus for direct calculation. They usually give the value or show a simple band sequence.

Q&A Discussion Prompts (Session 4):
- "If you see a component in a radio that looks like a small can with + and - markings, what is it likely to be, and why is the marking important?" (Electrolytic capacitor, polarity).
- "What's the main difference in function between a resistor and an inductor when dealing with AC signals?" (Resistor always resists, inductor's opposition increases with frequency).
- "If you wanted to measure the current being drawn by a small light bulb powered by a battery, how would you connect your ammeter?"