Your Ham Shack: Station Equipment & How We Modulate
Core Station Equipment (T7A):
  - Transmitter (Tx): Generates RF, adds info (modulates), amplifies, sends to antenna.
  - Receiver (Rx): Captures RF, selects, extracts info (demodulates), amplifies for listening.
  - Transceiver: Combines Tx and Rx in one unit. (HT, Mobile, Base).
Common Station Accessories (T7B):
  - Power Supply: Converts AC to DC for the radio (e.g., 13.8V DC).
  - SWR Meter: Measures antenna system match (Standing Wave Ratio). Low SWR is good.
  - Dummy Load: Non-radiating 50 Ohm load for off-air transmitter testing.
  - Antenna Switch: Selects between multiple antennas/radios.
  - Antenna Tuner (Transmatch): Matches impedance between radio and antenna system.
Common Radio Controls (T7C):
  - Tx: Power Output (use minimum necessary!), Mic Gain.
  - Rx: Volume, Squelch (mutes noise), RIT/Clarifier (fine-tunes receive frequency).
Modulation: Adding Information to a Carrier Wave (T8A, T8B):
  - AM (Amplitude Modulation): Varies signal amplitude.
  - SSB (Single Sideband): Efficient AM variant; uses LSB (Lower Sideband, common <10 MHz HF) or USB (Upper Sideband, common >10 MHz HF, VHF/UHF).
  - FM (Frequency Modulation): Varies signal frequency. High fidelity, common on VHF/UHF.
    - Deviation: Amount of frequency change. FM uses more bandwidth.
  - CW (Continuous Wave / Morse Code): On/off keying of carrier wave. Very efficient.
  - Digital Modes: Computer + radio. Examples:
    - RTTY: Older text mode.
    - PSK31: Keyboard-to-keyboard text chat.
    - FT8/FT4: Weak signal, automated text contacts.
    - Packet Radio: Data in "packets"; used for text, APRS.
    - APRS (Automatic Packet Reporting System): Real-time position/data reporting (VHF).
    - SSTV (Slow Scan TV): Transmits still images.
References:
  - ARRL Ham Radio License Manual, Chapters on Station Equipment and Modulation Modes.
  - https://dxcluster.ha8tks.hu/hamgeocoding/
  - http://casperarc.net/wiki/index.php?title=IRLP_DTMF
  - https://www.aprs.org/
  - https://sarc.org.au/fl-digi/
  - https://www.contestcalendar.com/perpetualcal.php