Review – Session-4
T6A – D, T7D

T6A03
What electrical parameter is controlled by a potentiometer?
A. Inductance
B. Resistance
C. Capacitance
D. Field strength

T6A10
Which of the following battery chemistries is rechargeable?
A. Nickel-metal hydride
B. Lithium-ion
C. Lead-acid
D. All these choices are correct

T6B03
Which of these components can be used as an electronic switch?
A. Varistor
B. Potentiometer
C. Transistor
D. Thermistor

T6B12
What are the names of the electrodes of a bipolar junction transistor?
A. Signal, bias, power
B. Emitter, base, collector
C. Input, output, supply
D. Pole one, pole two, output

T6C01
What is the name of an electrical wiring diagram that uses standard component symbols?
A. Bill of materials
B. Connector pinout
C. Schematic
D. Flow chart

T6C12
Which of the following is accurately represented in electrical schematics?
A. Wire lengths
B. Physical appearance of components
C. Component connections
D. All these choices are correct

T6D02
What is a relay?
A. An electrically-controlled switch
B. A current controlled amplifier
C. An inverting amplifier
D. A pass transistor

T6D08
Which of the following is combined with an inductor to make a resonant circuit?
A. Resistor
B. Zener diode
C. Potentiometer
D. Capacitor

T7D03
When configured to measure current, how is a multimeter connected to a component?
A. In series
B. In parallel
C. In quadrature
D. In phase

T7D10
What reading indicates that an ohmmeter is connected across a large, discharged capacitor?
A. Increasing resistance with time
B. Decreasing resistance with time
C. Steady full-scale reading
D. Alternating between open and short circuit