Intro to Tech - Session-5
        Tate, KA7O
        ka7o@casperarc.net

---
Review: Session - 4
- Quiz handed out
- No grades kept
- Just for you
- Nope, not all the same letter this time <g>

---
Subelements T7A, T7B, T7C
- T7A: Transmitters, receivers, transceivers
  - basic block diagrams & functions
- T7B: Common station accessories
  - power supply, dummy load, SWR meter, antenna switch, antenna tuner
- T7C: Controls
  - Transmitter
    - power output, microphone gain
  - receiver
    - volume, squelch, RIT

---
Subelements T8A
- T8A: Modulation basics
  - Amplitude Modulation (AM)
    - Single Sideband (SSB)
      - LSB/USB
  - Frequency Modulation (FM)
    - Deviation
    - Bandwidth

---
T8A – cont.
- Continuous Wave (CW)
- Common digital modes
  - e.g., PSK31, FT8, RTTY
  - packet radio, APRS,
  - image modes (SSTV)

---
T8B
- Amateur satellite operation
  - Doppler Shift
  - Basic orbits
  - Operating protocols
  - Modulation mode selection
  - TX Power considerations
  - Telemetry & Telecomand
  - Tracking Programs
  - Beacons

---
T8B cont.
  - Uplink & downlink modes
  - Spin Fade
  - LEO
  - Setting Uplink Power

---
T8C
- Operating activities
  - Radio Direction Finding – RDF
  - Contests
  - Linking over Internet
  - Exchanging Grid Locators

---
T8D
- Non-voice and digital communications
  - Image signals and NTSC
  - CW
  - PSK
  - APRS
  - Error Detection and Correction
  - Radio Networking (AX.25, packet)
  - Digital Mobile Radio – DMR
  - WSJT modes
  - Broadband - Hamnet

---
Transmitters, Receivers and Transceivers
- Transmitter (TX)
  - Generates a Radio Frequency (RF) signal
    - Uses an Oscillator for this
  - Modulate the signal (Adds information)
    - Voice
    - Data
    - CW
  - Amplifies it (RF/Power Amplifier)
  - Sends it to antenna

---
AM Transmitter

---
Receiver

---
Transceiver
- Function
  - Combines a transmitter and receiver in ONE unit
    - Uses as TX/RX switch to change function
  - Most modern ham radios are transceivers
  - Often share some circuits
    - Power supply
    - Display
    - Sometimes Antenna Switching

---
Transceivers
- Various forms
  - Handheld Transceivers (HTs)
    - Typically V/UHF
  - Mobile Transceivers
    - For use in vehicles
    - More power than Hts
  - Base or Fixed station Transceivers
    - More power
    - More features

---
HTs
Far and away the most popular

---
Mobile Radios

---
Base/Fixed Station

---
Some Terms
- Sensitivity
  - Ability of a receiver to detect a signal
- Mixer
  - Combines a frequency with another
- Selectivity
  - Differentiate between multiple signals
- Oscillator
  - Generates a signal at a
    specific frequency

---
Terms (cont.)
- Transverter
  - Converts RF to another band
- Push to Talk (PTT)
  - Switches from RX to TX
- Modulation
  - Combines speech with an RF signal
    - Amplitude and deviation (am/fm)
- RF Power Amplifier
  - Increases output power

---
Terms (cont.)
- Single Side-band (SSB)
  - An AM signal that has had either the upper or lower sideband removed
  - Allows for more efficient power use and less interference
- Pre-amplifier
  - Goes in front of a receiver,
    strengthens weak signals
- Receive Incremental Tuning (RIT)
  - A fine tuning adjustment used in SSB

---
Common Problems
- Overload
  - Too much RF signal for a stage
    - Add filtering
- Overdrive
  - Too much audio input (Mic Gain)
    - Causes distortion or over-deviation
    - Lower audio input level – move back
- RFI -Radio Frequency Interference
  - When a receiver can’t filter/select desired signal due to overload, harmonics or spurious emissions

---
Common Problems
- RF Feedback
  - Transmitted RF output being ‘captured’ by transmiter’s input audio stage
    - Causes severe distortion
    - Correct by adding a ‘current choke’, such as a ferrite on the mic cable
- Fundamental Overload
  - Broadcast or TV transmitter or
    it’s harmonics causing too much
    un-wanted signal into your antenna

---
Common Problems
- Fundamental Overload (cont.)
  - Can be reduce, if not eliminated by adding a filter to block the unwanted signal
  - Useful if your neighbors complain about hearing your AM/SSB signals in their audio equipment
  - Often called a “Band Pass” or
    “Band Reject” filter
    - Depends on design and
      desired action

---
Common Problems
- Neighbor complaints
  - Not nearly so common for TV reception due to change from NTSC to digital TV
- If you get a complaint
  - Verify your equipment is working correctly
  - Test with your own TV or broadcast radio
  - Good to make an effort
  - Ultimately not up to you to correct for poorly designed or faulty consumer equipment

---
Common Problems (cont.)
- Still possible for neighbors to receive TV Interference on copper cable
  - Connectors loose or improperly installed
  - Causes distortion of their signal
- Other hams say your signal is bad
  - Verify your TX is On Frequency
  - In an HT or Battery station, could be caused by batteries being low
  - You’re simply too close to them
    - Move – that’s a bad location?

---
Common Problems
- If your neighbor’s ‘stuff’ is causing you problems
  - Don’t accuse, you want them on your side
  - Work with them to ID the source
  - Inform them that FCC rules prohibit them causing interference, the law is on your side
  - Doubly Verify your gear is
    working correctly!

---
Shack Gear
- Power Supply
  - Most ham gear doesn’t plug into a wall
- SWR Meter
  - Measures antenna system match to TX
- Dummy Load
  - Lets you test transmitters with out
    a signal going out
  - Non-inductive resistor on
    a heat-sink

---
Dummy Load

---
Shack Gear
- Feed line
  - Typically COAX
  - Susceptible to moisture
  - Coax, nominally 50 Ohm impedance
  - Usually UV resistant when intact
- Two basic types of COAX
  - Foam or Solid Dielectric
  - Air Dialectric
    - Requires special techniques & fittings

---
Types of COAX

---
Shack Gear
- All feedline is imperfect
  - Will have some losses, seen as RF converted to heat along feedline
  - Moisture in feedline will radically change it’s characteristics, often rendering it useless
  - Typically exposed to sunlight, resulting in natural degradation and water contamination

---
Shack Gear
- Antenna Switch
  - Allows selecting between multiple antennas, e.g. if single band antennas
- Antenna Tuner
  - Transmatch
  - Matches impedance between radio
    and antenna system
- Antenna Analyzer
  - Provides more information on antenna system, including resonance by freq

---
Antenna Switch

---
An Antenna Tuner

---
Useful Shack Gear
- Many new tools, such as NanoVNA and TinySA now on the market
- Tools sold to hams may be easier to use, but can be limited in information provided
- Test equipment specifically for radio is available on the 2nd hand market
- Can get very expensive, fast

---
Rigexpert analyzer
MSRP – $1,199.95

---
NanoVNA
MSRP – aprox $120.00

---
Typical Controls
- Transmitter
  - RF Gain
    - Adjust output power
    - Rules require you use the minimum
  - Mic Gain
    - Don’t over drive your transmitter
  - Band
    - Adjust TX frequency to another band
  - Frequency
    - Choose frequency within a band

---
Typical Controls
- Receiver
  - Volume
  - Squelch (mutes noise)
  - RIT/Clarifier
    - Fine tuner
  - Band
    - Select a different band
  - Frequency
    - Select desired frequency within band

---
Break Time
- That’s been a goodly amount of info
- LOTS more to come!
- Go, be refreshed – we’re going deep into the tech of some things
10 minutes, please

---
Modulation
- Amplitude Modulation (AM)
  - Voice mixed with carrier by changing the amplitude of the carrier to match the voice envelope
  - Single Sideband is a type of AM
    - One or the other sideband is filtered out
      of transmitted signal
    - More efficient use of TX power
    - More efficient use of bandwidth
      - Typically 3Khz wide
  - USB > 10Mhz LSB < 10Mhz

---
Modulation
- Frequency Modulation - FM (Phase Modulation PM)
  - The RF carrier itself is changed according
    to the audio envelope
  - Much better reproduction of original signal
  - “Capture Effect” locks in only one signal
    - May be an advantage with weak signals
  - Wider bandwidth than AM or SSB
    (10 to 15Khz)
  - Not as good as SSB for long-distance or weak signal reception
  - Commonly used for V/UHF and repeaters

---
Side Bar - Signal Imagery
- Two types
  - Time domain (Oscilloscope)
  - Frequency domain (spectrum analyzer)
- Now, doable in software
  - Waterfall displays (FFT – FTW!)
- Some displays show both time and
  Frequency domain

---
Modulation

---
FM Voice

---
CW or “Morse” Code
- Oldest of all the modes
- One of the narrowest - 150Hz
- Reliant on a ‘good ear’ to be understood if/when conditions are poor
  - Some OG guys are dang near Magic!
- Can be read or sent by software
  - But, experienced operators
    can tell and some are likely to avoid
    such contacts

---
Continuous Wave (CW)

---
Digital Modes
- Radio Teletypwriter (RTTY)
  - Older text mode
- Phase Shift Keying, 31 baud) PSK31
  - Keyboard to keyboard text chat
- Franke-Taylor design) FT8/FT4
  - Weak Signal, automated text
- Packet Radio – AX.25
  - Older connected mode text

---
CW – SSB – Digital

---
Digital Modes
- Automatic Packet Reporting System (APRS) https://www.aprs.org/
  - Real-time position/data via packet
- Slow Scan TV (SSTV)
  - Still Images
  - Narrower than NTSC’s 6Mhz
  - Can take up to 30 seconds or
    more to send a single image

---
Digital Modes
- Used to need special hardware to generate modes – such as an “RTTY Modem”
- Now, we use software to drive a sound card
  - The sound is fed into an AM or FM transmitter and the resulting
    RF signal is what the old
    hardware would have generated

---
Software
- FLDIG (Fast Light Digital)
  - CW, PSK, MFSK, RTTY, Hell, DominoEX, Olivia, and Throb
- Ham Radio Deluxe
  - CW, RTTY, SSTV, PSK31, MT-63, and more
- WSJT-X
  - JT65, JT9, and JT4
- Packet – AX.25
  - Direwolf, SoundModem and QTSoundModem

---
Fldigi

---
Waterfalls of modes

---
Some Other Modes
- Digital Mobile Radio – DMR (Motorola)
- Wires-X (Icom)
- Fusion (Yaesu)
All still require specific hardware
Such modes are rarely seen on HF
They are not compatible with
each other – proprietary lock-in

---
Connect Sound card and radio
- Does not require special hardware
- Yet, many interface devices available
  - SignaLink USB
  - DigiRig
    - Several versions and models of each
Though not required, they do make getting all the things setup easier
Big challenge in setting levels
Interface devices make this much easier

---
SignaLink USB

---
Amateur satellite operation
- Typical Data Received
  - Information on the Health and Status of the satellite
  - Sometimes encrypted or obfuscated
  - Voice repeaters
  - Text messages (store ‘n forward)
- Avoid excessive power
  - May desense the receiver
  - Block others from accessing

---
Satellite tracking programs
- Gpredict
  - Free
- HRD Satellite Tracker
  - Part of Ham Radio Deluxe - HRD
- Nova
  - Free
- Orbitron
  - Freeware (cardware)
- Satscape
  - Freeware

---
Satellite Tracking
- Real time maps or charts of passes
  - See current times and where any particular satellite will be in your sky
- Pass Predictions
  - Provide a table of times, azimuth and distances in the future
- Many also provide Doppler Info
  - How to adjust your TX and RX to effectively use the satellite

---
Gpredict

---
Keplerian Elements
- Freely available over the Internet
- Datasets the software uses to know and calculate current and future position and track of satellites
- Often also includes frequency information to calculate Doppler Shift
- Doppler Shift
  - An observed change in signal
    frequency caused by relative motion

---
Modes
- Each ‘bird’ is specific
- Commonly:
  - SSB
  - FM
  - CW/Data
- Some sats have their own proprietary modes
- Many have websites with details

---
Repeaters in the Sky
- Many us “U/V” mode
  - Uplink in the 70cm band
  - Downlink in the 2m band
- A few require SSB instead of FM on U/V
- Some even use their own methods

---
Satellite Beacons
- Just a simple transmission indicating the satellite is active and information to include status of the satellite’s health
- Can be used to detect “Spin Fade”
  - Changes in signal strength caused by rotation of the satellite and it’s antennas
- Some call these ‘Heart Beat’
  beacons

---
LEO Satellites
- Low Earth Orbit - LEO
- Due to their lower orbits, move quite fast
  - As an example, ISS goes around the world every 90 minutes
  - May be in your sky and viewable for only about 9 minutes each pass
- Satellites in higher orbits take longer
  to go around the planet and will be
  viewable for longer each pass
  - To the point of being Geosynchronous

---
Uplink Power Levels
- Watch your downlink signal
  - Should be close to the beacon’s level
  - Adjust so you’re not stronger
  - Remember, there are no obstructions
    Only distance – low power often works better than higher power
    - Minimizes distortion

---
Unlicensed reception
- Basic rule of Radio (in the US)
  - If you can receive it, it’s legal to receive, goes for anyone
  - Few special bands/frequencies where that doesn’t apply such as cell phone bands
  - Attempting to decrypt any encrypted signal is a violation

---
Locating Interference
- Using Radio Direction Finding methods (RDF) can help locate sources of interference
  - Often use directional antennas
  - Body nulls or shielding
  - Special equipment
    - KrakenSDR is one of the better

---
KrakenSDR

---
Contesting
- For some (many?) their whole reason to be an amateur operator
- Basically, make as many contacts as possible in a fixed time
  - Contacts (QSOs) are logged at each end
  - Logs are compared to verify QSO
- Awards – plaques, certificates
- Good practice
- Can become QUITE competitive

---
Contest Calendar

---
Exchanges
- Most contests use a prearranged exchange of information for logging
  - Have their own rules
- Helps speed things along
- Send the minimum information needed for proper ID and exchange
- eg. Field Day
  - We send:
    “W7VNJ Three Alpha Wyoming”

---
Grid Locators
- Often used for V/UHF contests
- A way of sending your location and defining an area
- Maidenhead Gridsquares
  - World is broken into sections
  - Easier to exchange that Lat Longs!

---
A Gridsquare Locator

---
4 characters
- Typical locator is only 4 characters
  - Typical all that’s used for contests
- For example – here in Casper, we are
        DN62
- For my home (QTH)
  - DN62tt is close
  - Next pair are lower case
  - DN62tt19 gets you in tighter
  - Never seen more than 8

---
World Gridsquare Map

---
DN

---
DN62tt

---
DN62tt19

---
IRLP
- Internet Radio Linking Project
  - Way to connect systems, like repeaters over the Internet using VOIP
- Use DTMF codes from your radio to select remote node and close link
- Casper has an IRLP node
- Access the IRLP Gateway via the 449.575 repeater
- Tightly monitored, known for good audio

---
EchoLink
- Another method for connecting systems over the Internet with VOIP
- Does NOT require a radio
  - Can be accessed with only a computer
  - Does require your call be registered before you can access the system
  - Not too hard to spoof
  - Known for poor audio

---
DMR
- Requires hardware
- Allows for dense use of bandwidth using Time-multiplexed channels (2) on a single 12.5kHz channel
- Supports “Talk Groups”
  - Limits what radios will work at any one time
  - groups share a channel
    without interfering with each other

---
WSJT-X
- Very low signal levels
  - Often and commonly below noise floor
- Works well for
  - Earth-Moon-Earth (EME)
  - Weak Signal beacons for propagation study
  - Meteor Scatter
- Not so good for conversation
  - But doable - slowly

---
ARQ
- Automatic Repeat reQuest
- an error correction method used in data transmission within amateur radio
- Allows for automatic QSOs
- Set it all up – leave it alone
- Come back later and see what exchanges have been made
- Useful for difficult conditions

---
APRS
- Invented by Bob Bruninga, WB4APR (SK) to track Naval Cadets on sailboats in a nearby bay
- Has methods for sharing
  - GPS Location Information
  - Text messaging
  - Weather data
- All traffic in North America
  - 144.390Mhz

---
APRS
- Transmissions, being AX.25, include
  - Check Sum for error detection
  - Header contains sender’s callsign
  - Header contains target callsign
    - In APRS these are ‘generic’, not specific
  - If error is detected, can send an automatic re-send request
  - Must be configured for ARQ

---
APRS Frequencies

---
NTSC
- How old, analog Color Television was transmitted
- Considered a ‘Fast Scan’ mode due to refresh rate of the image
- Has been used on the Amateur Bands
- Wide bandwidth 6 Mhz wide
  - Spectrum for 6 Mhz bandwidth
    is sparse
  - Most limited to 5 Mhz
- Typically seen in UHF

---
Broadband - Hamnet
- An implimentation of a mesh network
- Not unique to Amateur Radio
- Uses commercial WiFi hardware to automatically build a data mesh
- Members join and drop automatically
- Allows
  - Extending range
  - Error detection/correction
  - Servers - messaging

---
Phase Shift Keying - PSK
- Commonly used - PSK31
- First computer aided mode to be usable near or even below the noise floor
- Was QUITE popular for a few years
- However, due to lack of typing skills, most have abandoned texting for
  ‘Macro Exchanges’

---
That’s enough for this one
- LOTS of new information!
- See the handout
- Follow up and keep at those practice tests!
Any questions – feel free to holler
Tate, KA7O
ka7o@casperarc.net