Student Handout 6: Antennas, Safety, Practices & Final Review
Antennas (T9A):
  - Function: Radiate/receive RF energy. Length is key for resonance.
  - Polarization: Orientation of electric field (Vertical, Horizontal, Circular). Match polarization for best signal. Most VHF/UHF FM is vertical.
  - Common Types:
    - Half-wave Dipole: ≈f(MHz)468​ feet long. Fed at center. Balanced.
    - Quarter-wave Vertical: Needs a ground plane (e.g., car body, radials). Unbalanced.
    - Yagi (Beam): Directional, provides gain.
Feed Lines & Connectors (T9B):
  - Coaxial Cable (Coax): Common feed line (e.g., RG-58, RG-8X, RG-213). Characteristic impedance usually 50 Ohms. Loss increases with frequency and length.
  - Connectors: PL-259/SO-239 (UHF), BNC, SMA.
  - SWR (Standing Wave Ratio): Measure of impedance match. Low SWR (e.g., 1:1 to 1.5:1) is best.
  - Antenna Tuner: Helps match antenna system impedance to transmitter.
  - Balun: Matches balanced antenna (dipole) to unbalanced coax.
RF Exposure Safety (T0A):
  - High RF levels can be harmful (tissue heating). Follow FCC MPE limits.
  - Perform RF exposure evaluation for your station.
  - Precautions: Maximize distance from antennas, use minimum power, limit exposure time.
Electrical Safety (T0B):
  - Use 3-wire AC cords and properly wired outlets. Use GFCIs where appropriate.
  - Ground all station equipment to a common earth ground (ground rod).
  - Use correct fuses. Beware of high voltages inside equipment, even when off.
Antenna Installation Safety (T0C):
  - EXTREME DANGER: OVERHEAD POWER LINES! Maintain very large clearances.
  - Use climbing safety gear and helpers if climbing. Never climb alone or in bad weather.
  - Install lightning protection: Ground towers/masts, use lightning arrestors on feed lines. Disconnect equipment during storms.
Radio Frequency Interference (RFI) (T4):
  - Interference to/from other electronic devices.
  - Fundamental Overload: Strong signal overwhelms device.
  - Harmonics: Unwanted signals from your transmitter. Low-pass filter can help.
  - Use good grounding, ferrite chokes, filters. Cooperate with neighbors.
Exam Day & Beyond:
  - Bring Photo ID, FRN, exam fee, pencils, basic calculator.
  - 35 multiple-choice questions, pass with 26 correct.
  - Once your call sign is in the FCC ULS database, you can operate!
  - Join a club, get on the air, keep learning!
References:
  - ARRL Ham Radio License Manual, Chapters on Antennas, Safety, Operating Practices.
  - FCC Part 97 Rules & OET Bulletin 65 (RF Exposure).
    https://transition.fcc.gov/oet/info/documents/bulletins/oet65/oet65.pdf
  - https://www.cdt21.com/design_guide/antenna-types-and-parameters/
  - https://www.arrl.org/rf-exposure
  - https://www.arrl.org/rf-exposure-calculator
  - https://www.electronics-notes.com/articles/antennas-propagation/vertical-antennas/five-eighths-wavelength-vertical.php
  - https://www.n1fd.org/2019/11/12/the-amazing-20m-coil-shortened-shower-rod-dipole/
  - https://www.qsl.net/w4sat/five8th.htm
  - https://www.arrl.org/fcc-rf-exposure-regulations-the-station-evaluation