Review Session – 5

T7A08
Which of the following describes combining speech with an RF carrier signal?
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering

T7A11
Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter power amplifier
C. Between the transmitter and the antenna tuner
D. At the output of the receiver audio amplifier

T7B03
Which of the following can cause radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All these choices are correct

T7B09
What should be the first step to resolve non-fiber optic cable TV interference caused by your amateur radio
transmission?
A. Add a low-pass filter to the TV antenna input
B. Add a high-pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV feed line coaxial connectors are installed properly

T7C02
Which of the following is used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter

T7C04
What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
A. 50:50
B. Zero
C. 1:1
D. Full Scale
T8A02
What type of modulation is commonly used for VHF packet radio transmissions?
A. FM or PM
B. SSB
C. AM
D. PSK

T8A06
Which sideband is normally used for 10 meter HF, VHF, and UHF single-sideband communications?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Inverted sideband

T8B03
Which of the following are provided by satellite tracking programs?
A. Maps showing the real-time position of the satellite track over Earth
B. The time, azimuth, and elevation of the start, maximum altitude, and end of a pass
C. The apparent frequency of the satellite transmission, including effects of Doppler shift
D. All these choices are correct

T8B07
What is Doppler shift in reference to satellite communications?
A. A change in the satellite orbit
B. A mode where the satellite receives signals on one band and transmits on another
C. An observed change in signal frequency caused by relative

T8C01
Which of the following methods is used to locate sources of noise interference or jamming?
A. Echolocation
B. Doppler radar
C. Radio direction finding
D. Phase locking

T8C06
How is over the air access to IRLP nodes accomplished?
A. By obtaining a password that is sent via voice to the node
B. By using DTMF signals
C. By entering the proper internet password
D. By using CTCSS tone codes

T8D03
What kind of data can be transmitted by APRS?
A. GPS position data
B. Text messages
C. Weather data
D. All these choices are correct

T8D09
What is CW?
A. A type of electromagnetic propagation
B. A digital mode used primarily on 2 meter FM
C. A technique for coil winding
D. Another name for a Morse code transmission

T8D12
Which of the following best describes an amateur radio mesh network?
A. An amateur-radio based data network using commercial Wi-Fi equipment with modified firmware
B. A wide-bandwidth digital voice mode employing DMR protocols
C. A satellite communications network using modified commercial satellite TV hardware
D. An internet linking protocol used to network repeaters