Antennas, Safety, Practices & Final Review
- Time Allotment: 60 minutes instruction, 30 minutes Q&A/Discussion
- Learning Objectives:
  - Understand basic antenna types (dipole, vertical, Yagi), polarization, impedance, and SWR.
  - Identify key safety concerns: RF exposure, electrical safety, antenna/tower safety.
  - Understand good operating practices like dealing with RFI and proper grounding.
  - Review key concepts for the exam and know what to expect on exam day.
Materials Needed (Teacher's Note):
  - Whiteboard or projector.
  - Handout 6.
  - End-of-Class Feedback Forms.
  - Optional: Pieces of coaxial cable, different types of antenna connectors (PL-259, BNC, SMA), pictures of antenna installations (good and bad, for safety discussion). A simple dipole made of wire.
Key Topics Covered (Corresponds to Subelements T9A-B, T0A-C, T4A,B,E, T8C-D and exam prep):
  - Subelement T9A: Antenna basics: radiation patterns, polarization (vertical, horizontal, circular). Common antennas: dipole, quarter-wave vertical, Yagi (beam).
  - Subelement T9B: Feed lines (coax types, characteristics, losses), connectors. SWR (review), impedance matching, antenna tuners (review). Baluns.
  - Subelement T0A: RF exposure safety: MPE limits, SAR, station evaluation, precautions (distance, power, duty cycle).
  - Subelement T0B: Electrical safety: AC/DC hazards, grounding (station and AC), fuses, interlocks, GFCIs.
  - Subelement T0C: Antenna installation safety: overhead power lines (CRITICAL!), climbing safety, lightning protection (ground rods, arrestors).
  - Subelement T4A, T4B, T4E (selected topics): Interference (RFI – to/from consumer electronics), grounding for RF and lightning.
  - Exam day procedures, what happens after passing.
  - Final Q&A and encouragement.
Teacher's Script (Outline & Key Points):
(0-20 min) Antennas & Feed Lines: Your Gateway to the Airwaves (Subelements T9A, T9B)
- "Welcome to our final session! Today we tackle the antenna – arguably the most important part of your station. A great radio with a poor antenna won't perform well, but even a modest radio with a good antenna can work wonders."
- Subelement T9A: Antenna Basics & Common Types
  - Function: Converts electrical RF energy from your transmitter into radio waves, and vice-versa for your receiver. It's a transducer.
  - Resonance: Antennas work best when they are resonant (electrically "tuned") for the frequency of operation. Physical length is critical.
  - Radiation Pattern: How an antenna radiates energy in different directions (e.g., omnidirectional like a vertical, or directional like a Yagi).
  - Polarization: The orientation of the electric field of the radio wave.
    - Vertical Polarization: Antenna elements are vertical (e.g., most mobile whip antennas, HT "rubber duck" antennas when held vertically). Common for VHF/UHF FM.
    - Horizontal Polarization: Antenna elements are horizontal (e.g., many HF dipoles, some VHF/UHF SSB/CW beam antennas).
    - For best results, both stations should use the same polarization. Mismatched polarization can cause significant signal loss (20 dB or more).
    - Circular Polarization: Used for satellite work (less susceptible to spin fading).
  - Common Antenna Types:
    - Half-wave Dipole: Very common, fundamental antenna. Two quarter-wavelength elements fed in the center. Length (feet) ≈frequency in MHz468​. (If you have a wire dipole, show it). Typically horizontally polarized.
    - Quarter-wave Vertical: One quarter-wavelength radiating element working against a ground plane (e.g., car body, or a set of radial wires on the ground or elevated). Typically omnidirectional and vertically polarized.
    - Yagi (Beam Antenna): Directional antenna. Has a "driven element" (like a dipole), a "reflector" behind it, and one or more "directors" in front. Provides gain (concentrates power) in one direction.
    - "Rubber Duck" antenna: Compact, flexible antenna found on handhelds. Convenient but much less efficient than a full-size antenna.
Subelement T9B: Feed Lines, Connectors, Impedance, SWR, Baluns
  - Feed Line: Transmits RF energy between radio and antenna with minimal loss.
    - Coaxial Cable ("Coax"): Most common. Center conductor, dielectric insulation, braided shield (outer conductor), outer protective jacket. (Show a piece).
      - Has a characteristic impedance (e.g., 50 Ohms for most ham use, 75 Ohms for TV/cable). Important to match this to radio and antenna.
      - Common types: RG-58 (thinner, more lossy, okay for short VHF/UHF runs), RG-8X (better), RG-213 or LMR-400 (thicker, lower loss, good for longer runs or higher frequencies). Loss increases with frequency and length.
  - Connectors: Used to connect coax to radios and antennas.
    - UHF Connectors (PL-259 plug / SO-239 jack): Common on HF/VHF base/mobile radios. Not truly "UHF" by modern standards, and not weatherproof.
    - BNC: Bayonet style, good for VHF/UHF, test equipment.
    - SMA: Tiny, threaded, common on HTs.
  - Impedance Matching & SWR (Review):
    - Most transmitters expect to see a 50 Ohm load. Antennas also have an impedance at their feedpoint (e.g., a dipole in free space is about 72 Ohms, a vertical over good ground is ~35 Ohms).
    - SWR (Standing Wave Ratio): Measures the impedance mismatch. 1:1 is perfect. High SWR means power is reflected, lost, and can damage transmitter.
    - Antenna Tuner (Review): Helps match the system impedance to 50 Ohms for the radio.
  - Balun ("Balanced to Unbalanced"): A device used to match a balanced antenna (like a dipole) to an unbalanced feed line (like coax). Helps prevent feed line radiation and improves antenna performance.
(20-40 min) Safety First! A Crucial Topic (Subelements T0A, T0B, T0C)
- "Ham radio is a very safe hobby if we understand and respect the potential hazards and take sensible precautions. This is a VERY important section."
- Subelement T0A: RF Exposure Safety ("Getting Cooked")
  - High levels of RF energy can be harmful to humans (primarily by heating body tissue). Effects depend on frequency, power density, and duration of exposure.
  - MPE (Maximum Permissible Exposure): FCC-established limits for RF exposure to protect people.
  - SAR (Specific Absorption Rate): A measure of the rate at which RF energy is absorbed by the body.
  - Station Evaluation: YOU are responsible for ensuring your station complies with MPE limits. This involves a simple evaluation (worksheets/calculators available from ARRL/FCC). Required if running > certain power levels or with high-gain antennas, especially on VHF/UHF.
  - Precautions:
    - Distance is your friend: RF power density decreases rapidly with distance from the antenna. Keep antennas away from areas where people (including neighbors) will be.
    - Use the lowest power necessary for communication.
    - Consider duty cycle (how much you transmit vs. listen).
    - For HTs, keep antenna away from head/eyes during long transmissions; use an external speaker/mic if possible.
Subelement T0B: Electrical Safety ("Getting Zapped")
  - AC Power Hazards: Household AC (120V in US) can be lethal.
    - Use 3-wire cords and properly wired outlets (ensure ground pin is connected).
    - GFCI (Ground Fault Circuit Interrupter): Recommended for outlets in potentially damp locations or outdoors.
  - Station Grounding (Electrical Safety & RF Performance):
    - Connect all metal cases of station equipment (radio, power supply, tuner) to a common ground point using short, heavy conductors (braid or copper strap is best).
    - This common ground point should then be connected to a good earth ground (e.g., 8-foot copper-clad ground rod driven into the earth outside). This helps prevent shocks and can reduce RFI.
  - Fuses & Circuit Breakers: Protect equipment and wiring from overcurrent/fire. Always replace with the exact same type and rating.
  - Interlocks: Safety switches that automatically cut power if equipment enclosures are opened (more common in high-power or older commercial gear).
  - Beware of high voltages inside equipment, especially power supplies and older tube-type gear, even when turned off (capacitors can store a lethal charge!).
Subelement T0C: Antenna & Tower Safety ("Falling & Frying")
  - OVERHEAD POWER LINES: THE #1 KILLER IN ANTENNA WORK.
    - NEVER install antennas, masts, or guy wires anywhere near power lines.
    - Maintain extreme clearance – at least 10 feet plus the full length of your antenna/mast if it were to fall.
    - Look up, look around! Identify all wires before starting. Assume ANY wire is a power line and is energized.
    - Do not use metal ladders near power lines.
  - Climbing Safety (Towers, Roofs):
    - If you must climb, use a proper climbing harness and safety equipment.
    - Inspect tower/mast and climbing gear before each climb.
    - Have at least one, preferably two, trained ground helpers. Never climb alone.
    - Don't climb in bad weather (wind, rain, ice, lightning).
    - Don't climb if tired or unwell.
  - Lightning Protection: Radio antennas are attractive to lightning.
    - Ground antenna support structures (towers, masts) directly to their own dedicated ground rods.
    - Use lightning arrestors on feed lines where they enter the house. These should also be grounded to the station ground system.
    - It's good practice to disconnect antennas and AC power from your station equipment during thunderstorms, even with arrestors.
Historical Anecdote/Reminder: "Many early radio experimenters faced significant electrical hazards, working with high voltages and crude equipment. Safety standards have evolved greatly. Hiram Percy Maxim, a founder of the ARRL, was an engineer who understood safety. The ARRL has always emphasized safe practices. Remember, no contact or experiment is worth your life or health."
(40-50 min) Good Operating Practices: Being a Good Neighbor (Subelement T4 - selected)
- "Being a good operator also means minimizing interference to others and from others."
- RFI (Radio Frequency Interference):
  - When your transmissions interfere with other electronic devices (TVs, stereos, telephones, computers, medical devices), OR when their devices generate noise that interferes with your radio reception.
  - Common Causes of Your Station Causing RFI:
    - Fundamental Overload: Your strong signal from a nearby antenna simply overwhelms the poorly shielded input of the affected device. (Often the fault of the affected device's design).
    - Harmonics: Your transmitter might be producing unwanted signals on multiples of your operating frequency (e.g., 2nd harmonic of 14 MHz is 28 MHz). A low-pass filter on your transmitter output can help reduce harmonics.
    - Poor station grounding or feed line issues.
  - Troubleshooting RFI:
    - First, ensure your own station is operating correctly (good grounding, no excessive SWR, filters if needed).
    - Work cooperatively and politely with your neighbor if they report a problem. Never be confrontational.
    - Ferrite chokes (snap-on beads or rings): Can be placed on power cords, speaker wires, data cables (both at your station and on the affected device) to suppress RF traveling on those wires.
    - Filters (e.g., high-pass filter for a TV, common mode choke for your feedline).
Grounding for RF and Lightning (Review): A good station ground system is crucial for minimizing RFI and for lightning protection.
(50-55 min) Exam Day & Beyond: What to Expect
"You've put in the effort, you've learned a lot! So, what happens at the exam session?"
  - Exam sessions are administered by teams of accredited Volunteer Examiners (VEs).
  - What to bring:
    - Photo ID (driver's license, passport).
    - Your FRN (FCC Registration Number) if you have one. If not, you can get one online from the FCC or register at the session.
    - The exam fee (VE teams are permitted to charge a small fee to cover costs, check with your local team).
    - Pencils. Basic (non-programmable) calculator is usually allowed (VEs will check).
    - (Optional) Any existing CSCEs (Certificates of Successful Completion of Examination) if you are upgrading.
  - You'll fill out NCVEC Form 605.
  - You'll take the 35-question multiple-choice Technician test (Element 2).
  - VEs will grade your test, usually right there at the session.
If You Pass:
  - Congratulations! You'll receive a CSCE.
  - The VEs will submit your application to the FCC.
  - Your new call sign will typically appear in the FCC ULS (Universal Licensing System) database online within a few days to a couple of weeks. You can legally operate once your call sign appears in the FCC database.
  - Get on the air! Start with local repeaters. Listen. Make your first contact.
  - Join a local ham radio club. This is the BEST way to learn more, get help (we call it "Elmering"), and participate in activities.
  - Consider ARRL membership for QST magazine, technical support, and to support the amateur service.
  - Keep learning! There's always more to discover in ham radio.
(55-60 min) Final Encouragement, Course Wrap-up & Feedback Forms
- "You are all well-prepared. Review your handouts. If you wish, try some online practice exams to get a feel for the question format (e.g., ARRL, HamStudy.org, QRZ.com, eHam.net – no endorsement of any particular one, many are good)."
- "During the exam: Read each question carefully. Eliminate obviously wrong answers first. Don't second-guess yourself too much. There is no penalty for guessing if you're unsure."
- "Thank you for your dedication and enthusiasm throughout this course! It's been a pleasure guiding you. I sincerely hope to hear many of you on the air soon with your new call signs!"
- "Before our final Q&A, please take a few minutes to fill out the feedback form. Your honest opinions will help improve future classes."
- Distribute feedback forms.
(60-90 min) Final Q&A and Discussion
- Address any lingering questions about any topic from the entire course.
- Discuss exam-taking strategies further if desired.
- Share resources for finding local clubs or exam sessions (ARRL website is a good starting point: http://www.arrl.org/find-a-club and http://www.arrl.org/find-an-amateur-radio-license-exam-session).
- Offer personal encouragement.

Teacher's Notes (Session 6):
- Safety is PARAMOUNT. Spend adequate time on RF exposure, electrical, and especially antenna installation safety. Use clear, strong warnings about power lines. Show pictures if possible of dangerous situations.
- SWR and Impedance: These can be confusing. Reiterate that SWR is a ratio indicating a match.
- RFI: Emphasize cooperation and good engineering practice. It's often not "your fault" but a shared issue.
- Reassure students about the exam. The goal is for them to feel confident and knowledgeable, not just memorizers.
- For the 55+ group: Antenna installation safety is particularly important. Strongly discourage risky installations or climbing without proper training and help. Emphasize simpler, safer antenna options.
- Practice Exams: While "no homework," suggesting online practice exams as a self-assessment tool for those who want it is fine, as long as it's optional.
- Celebrate their progress! This is the culmination of their learning.
Student Handout 6: Antennas, Safety, Practices & Final Review
Antennas (T9A):
  - Function: Radiate/receive RF energy. Length is key for resonance.
  - Polarization: Orientation of electric field (Vertical, Horizontal, Circular). Match polarization for best signal. Most VHF/UHF FM is vertical.
  - Common Types:
    - Half-wave Dipole: ≈f(MHz)468​ feet long. Fed at center. Balanced.
    - Quarter-wave Vertical: Needs a ground plane (e.g., car body, radials). Unbalanced.
    - Yagi (Beam): Directional, provides gain.
Feed Lines & Connectors (T9B):
  - Coaxial Cable (Coax): Common feed line (e.g., RG-58, RG-8X, RG-213). Characteristic impedance usually 50 Ohms. Loss increases with frequency and length.
  - Connectors: PL-259/SO-239 (UHF), BNC, SMA.
  - SWR (Standing Wave Ratio): Measure of impedance match. Low SWR (e.g., 1:1 to 1.5:1) is best.
  - Antenna Tuner: Helps match antenna system impedance to transmitter.
  - Balun: Matches balanced antenna (dipole) to unbalanced coax.
RF Exposure Safety (T0A):
  - High RF levels can be harmful (tissue heating). Follow FCC MPE limits.
  - Perform RF exposure evaluation for your station.
  - Precautions: Maximize distance from antennas, use minimum power, limit exposure time.
Electrical Safety (T0B):
  - Use 3-wire AC cords and properly wired outlets. Use GFCIs where appropriate.
  - Ground all station equipment to a common earth ground (ground rod).
  - Use correct fuses. Beware of high voltages inside equipment, even when off.
Antenna Installation Safety (T0C):
  - EXTREME DANGER: OVERHEAD POWER LINES! Maintain very large clearances.
  - Use climbing safety gear and helpers if climbing. Never climb alone or in bad weather.
  - Install lightning protection: Ground towers/masts, use lightning arrestors on feed lines. Disconnect equipment during storms.
Radio Frequency Interference (RFI) (T4):
  - Interference to/from other electronic devices.
  - Fundamental Overload: Strong signal overwhelms device.
  - Harmonics: Unwanted signals from your transmitter. Low-pass filter can help.
  - Use good grounding, ferrite chokes, filters. Cooperate with neighbors.
Exam Day & Beyond:
  - Bring Photo ID, FRN, exam fee, pencils, basic calculator.
  - 35 multiple-choice questions, pass with 26 correct.
  - Once your call sign is in the FCC ULS database, you can operate!
  - Join a club, get on the air, keep learning!
References:
  - ARRL Ham Radio License Manual, Chapters on Antennas, Safety, Operating Practices.
  - FCC Part 97 Rules & OET Bulletin 65 (RF Exposure).
  - ARRL website for RF safety, club, and exam session info.
Q&A Discussion Prompts (Session 6):
- "What's the single most important safety rule when planning to install an outdoor antenna?" (Stay far away from power lines).
- "If your neighbor says your radio is interfering with their TV, what's the first thing you should check at your own station?" (Grounding, SWR, look for loose connections, consider if a filter is needed).
- "What's one thing you're looking forward to doing once you have your license?"