Oscilloscopes, a basic introduction – hand out given to Casper Amateur Radio Club – W7VNJ on 19 Feb ‘25
Provided by: Tate - KA7O

#### **1. Basic Oscilloscope Setup**
**1.1 Connect the Probe**
- Attach the probe to the **Input Channel**.
- Connect the **ground clip** to your circuit’s ground.
- Touch the **probe tip** to the point where you want to measure the signal.

**1.2 Set the Vertical Scale (Volts/Div)**
- Use the **Volts/Div** knob to adjust the voltage range of the signal on the vertical axis.
- Start with a **higher setting** (e.g., 5V/div) and decrease if needed to better visualize the signal.
- Common settings:
  - Low power signals: 1V/div or less
  - Higher power signals: 5V/div or more

**1.3 Set the Horizontal Scale (Time/Div)**
- Use the **Time/Div** knob to adjust the amount of time displayed per division on the horizontal axis.
- Set a **small time scale** (e.g., 1 µs/div) for high-frequency signals, and a **larger time scale** (e.g., 1 ms/div) for lower frequencies.
- Example: For a 1 kHz signal, a setting of 1 ms/div is appropriate.

**1.4 Adjust the Trigger**
- Set the **trigger level** to stabilize the waveform. This ensures that the waveform starts at a consistent point each time it is drawn.
- Use **Auto** trigger mode to continuously capture signals, or **Normal** mode for more precise measurements when troubleshooting.

---

#### **2. Common Measurements**
**2.1 Frequency Measurement**
- Set the **Time/Div** so that one full cycle of the signal fits on the screen.
- Count the number of divisions per cycle and use the time scale to calculate the frequency:
  - **Frequency (Hz) = 1 / (Number of divisions × Time/Div)**
  - Example: If one cycle takes 5 divisions and the time base is 1 ms/div, then frequency = 1 / (5 ms) = 200 Hz.

**2.2 Voltage Measurement (Peak-to-Peak)**
- Count the vertical divisions between the highest and lowest points of the waveform (peak-to-peak).
- Multiply the number of divisions by the **Volts/Div** setting to get the peak-to-peak voltage.
  - Example: 4 divisions × 1 V/div = 4 V peak-to-peak.

---

#### **3. Troubleshooting Tips**
**3.1 Distorted Signals**
- If the waveform looks jagged or irregular, this could indicate interference, noise, or a fault in the circuit. Check connections and shielding.

**3.2 Modulation Check**
- For AM signals, check that the carrier wave is modulated evenly. The waveform should vary symmetrically in amplitude.
- For FM signals, the frequency of the waveform should vary smoothly.
**3.3 Oscillator Testing**
- When testing an oscillator, ensure the waveform is stable and consistent. Irregular waveforms could indicate issues with the circuit’s stability.

---

#### **4. Oscilloscope Quick Tips**
- **Start with Auto Mode**: Auto mode will help you capture most signals without too much adjustment. Once captured, you can refine settings for clarity.
- **Grounding is Key**: Always ensure the ground lead of your probe is properly connected to the circuit’s ground for accurate measurements.
- **Use the Probe Compensation Feature**: Oscilloscopes typically have a built-in calibration point to adjust the probe compensation. Ensuring proper compensation helps avoid signal distortion.

---

### **Video Tutorial Links for Further Learning**
Below are links to video tutorials that explain how to use oscilloscopes for ham radio applications and general signal analysis:

1. **How to Use an Oscilloscope** – Basic Overview
   - [YouTube: How to Use an Oscilloscope](https://www.youtube.com/watch?v=fgjHHsfPMOY)
   - This video provides a step-by-step guide for beginners on how to use an oscilloscope. It covers basic functions, setup, and waveform analysis.

2. **Oscilloscope Tutorial for Beginners**
   - [YouTube: Oscilloscope Tutorial for Beginners](https://www.youtube.com/watch?v=KLGfEopST6E)
   - A detailed beginner tutorial, walking through the essential controls and features of oscilloscopes, and showing live waveform examples.

3. **How to Measure Signals with an Oscilloscope**
   - [YouTube: Measure Signals with an Oscilloscope](https://www.youtube.com/watch?v=_bGyGgY7cmg)
   - This video focuses on practical measurements using an oscilloscope, such as measuring frequency, voltage, and troubleshooting signal distortion.

4. **Using an Oscilloscope for RF Troubleshooting**
   - [YouTube: RF Troubleshooting with an Oscilloscope](https://www.youtube.com/watch?v=sxtxE23jlv0)
   - Specifically targeted toward RF work, this video demonstrates how to use an oscilloscope to identify issues in RF circuits, such as signal interference and modulation problems.

5. **Modulation and Demodulation on Oscilloscopes**
   - [YouTube: Modulation on Oscilloscopes](https://www.youtube.com/watch?v=IjH82JVofCE)
   - This video explains how to visualize and analyze modulation types like AM and FM using an oscilloscope. Great for operators looking to check their signal's modulation quality.